## Slide 1: Benchmarking climate model top-of-atmosphere radiance in the 9.6mm ozone band compared to TES and IASI observations
Helen Worden, Andrew Conley,
Jean-François Lamarque, Steve Massie (NCAR),
Kevin Bowman (JPL),
Drew Shindell, (Duke Univ.)
Cathy Clerbaux, (LATMOS),
Pierre-François, Stamatia Doniki (ULB),
William Collins (UCB), Andrew Lacis (GISS)
Notes: Kevin talked about using TES radiative kernels to constrain climate models by looking at the radiative effects of differences in ozone. Here I will describe a more fundamental test of climate model predictions for ozone.

## Slide 2: Benchmarking O3 band TOA flux
The proposal addresses two primary questions:
What is the bias in IPCC climate model predictions of present day top-of-atmosphere (TOA) flux in the 9.6mm ozone band?
What is the impact of an ozone band TOA flux bias on present day tropospheric ozone flux sensitivity and pre-industrial to present day ozone radiative forcing estimates?
These will be tested with CAM-chem, RRTMG and GISS RT models using TES and IASI TOA flux and IRKs (Instantaneous Radiative Kernels)

## Slide 3: IPCC AR5 Radiative Forcing Definitions
IPCC AR5 Fig. 8.1
Used in <= AR4
+ AR5 (hatched)
Used in
AR5 (solid)
Direct Ozone RF
Preindustrial-to-present day: 0.35 W/m2
through 21st century: 0.89 W/m2
Indirect Ozone RF
Suppression of carbon uptake due to
plant damage: 0.6 to 1.1 W/m2
(Sitch et al., Nature, 2007)
Notes: ERF more realistic since tropopause can change as well (fixed SST) Calculation of ERF requires longer simulations with more complex models than calculation of RF, but the inclusion of the additional rapid adjustments makes ERF a better indicator of the eventual global mean temperature response, especially for aerosols.

## Slide 4: Trade-offs for air-quality controls and climate benefits
IPCC AR5
Need accurate measurements and model assessments
for informed policy decisions
Notes: Reductions in Nox and VOCs can add to warming through aerosol reductions and increasing methane lifetime

## Slide 5: Satellite IR O3 observations
CO2
H2O, N2O
O3
O3 (lnVMR) Jacobians
Frequency (cm-1)
Pressure (hPa)
-nW/cm2/sr/cm-1/ln(VMR)
TOA flux (W/m2)
LWRE (W/m2)
(long-wave radiative effect)
L(q,f,n) = TOA Radiance (W/cm2/sr/cm-1)
q
f
L(q,f)
R = anisotropy

## Slide 6: Spectral sensitivity of TOA flux to ozone and water vapor
H2O (ppm) Jacobians
Frequency (cm-1)
-nW/cm2/sr/cm-1/ppm
O3 (ppb) Jacobians
Frequency (cm-1)
-nW/cm2/sr/cm-1/ppb
H2O (lnVMR) Jacobians
Frequency (cm-1)
Pressure (hPa)
-nW/cm2/sr/cm-1/ln(VMR)
O3 (lnVMR) Jacobians
Frequency (cm-1)
Pressure (hPa)
-nW/cm2/sr/cm-1/ln(VMR)
TES obs. at 65°N, Aug. 2006
Worden et al., JGR, 2011
High spectral resolution is critical for separating O3 and H2O flux variability
Notes: With spectral resolution, we explicitly account for the effect of water vapor when we integrate over the O3 band Jacobians since the O3 Jacobians are zeroed out when there is a strong H2O line.

## Slide 7
Pressure (hPa)
Pressure (hPa)
H2O and O3 are radiatively coupled
H2O (lnVMR) Jacobians
Frequency (cm-1)
Pressure (hPa)
-nW/cm2/sr/cm-1/ln(VMR)
O3 (lnVMR) Jacobians
Frequency (cm-1)
Pressure (hPa)
-nW/cm2/sr/cm-1/ln(VMR)
65°N
-nW/cm2/sr/cm-1/ln(VMR)
-nW/cm2/sr/cm-1/ln(VMR)
6.2°N

## Slide 8: Potential Feedbacks to O3 RF from H2O
Understanding the feedback of water vapor on ozone RF (more water = less O3 RF) due to changes in the hydrological cycle from climate change will require the long-term measurements of IASI (A,B,C-2016) and IASI-NG (2021,2028,2035)
Water vapor LWRE in the IR ozone band
Worden et al., Nature GEO, 2008
IPCC AR5 FAQ 8.1 Fig. 1: Water cycle
with water vapour feedback ~7%/°C

## Slide 9: Initial Results: O3 band TOA Flux
All-sky August 2006 Average
Similar to OLR but only for the IR ozone band
This is a fundamental quantity, predicted by climate models, but never tested against observations.

## Slide 10: Initial Results: O3 band TOA Flux
RRTMG clear-sky (W/m2)
TES clear-sky (W/m2)
O3 band flux
comparison for
atmospheres
specified from
TES retrievals
Thanks to A. Conley (NCAR)
Known issues:
RRTMG band is 980-1080; TES band is 985-1080
(~1.1 to 1.7 W/m2)
different estimate of anisotropy (~5% difference w/ RRTMG higher)

## Slide 11: Initial Results: Tropos. O3 LWRE
IASI Tropospheric LWRE for 15 July, 2009
W/m2
0
-2
Thanks to S. Doniki, ULB, Brussels

## Slide 12: Initial Results: Tropos. O3 LWRE
Zonal averages: GISS RTM TOA flux sensitivity
and TES IRKs applied to same model differences
Latitude (deg)
DLWRE
Bowman et al., ACPD, 2013
Model-TES DLWRE comparison
Notes: Since the GISS model has a known dry bias in the upper troposphere at mid-latitudes, this could contribute to a higher sensitivity to changes in ozone as compared to TES.

## Slide 13: Initial Results: Tropos. O3 LWRE
Same atmosphere and surface conditions
Large differences for both clear and all-sky cases
From A. Conley, NCAR
Notes: RRTMG is the Rapid Radiative Transfer Model for GCMs from AER

## Slide 14: Conclusions
TOA flux from the IR Ozone band is a fundamental quantity in climate models that has not been compared to measurements.
Continuing the TES record with IASI data is critical for understanding present day to future changes in O3 radiative forcing, such as cloud coverage and water vapor feedback.
Initial results show differences for both flux and flux sensitivity between models and data that need to be reconciled.

## Slide 15: Backup

## Slide 16: Role of ozone in chemistry-carbon-climate coupling
Sitch et al,(2007), Nature
Direct effect:
Preindustrial-to-present day:
.35 [.25, .65] W/m2
Preindustrial through 21st century:
.89 W/m2
But O3 RF is also coupled to changes in H2O
Indirect effects:
Suppression of carbon
uptake by ozone damage to
plants could lead to additional
0.62 to 1.09 W/m2 CO2
radiative forcing
.89 W/m2

## Slide 17: H2O and O3 are radiatively coupled
Tropospheric ozone LWRE has a strong dependence on water vapor in the tropics.
Worden et al., JGR, 2011
Notes: different amounts of precipitable water vapor can change the tropical clear-sky LWRE of tropospheric ozone by up to a factor of 5. Regions of high humidity lead to a relatively optically thick atmosphere where ozone variability has little impact on TOA flux variability, i.e., ozone and water vapor are radiatively coupled in the TOA flux. Changes in the spatial distribution of ozone precursor emissions, e.g., increases in Asia, coupled with changes in the hydrological cycle from climate change will lead to different patterns of ozone forcing.

## Slide 18: Flux Estimate and Anisotropy
q
f
L(q,f)
Flux:
Anisotropy:

## Slide 19: Anisotropy Results
AIRS clear-sky anisotropy
models: 14 sub-scenes for
prec. wv, T_lapse, T_sur
Red = -5°-15°N
Green = 15°-30°N
Blue = 30°-45°N
X. Huang et al., JGR, 2008
TES anisotropy spectra
for clear-sky ocean scenes

## Slide 20: ANISOTROPY ESTIMATE
TES Anisotropy
R spectral dependence
R cloud OD dependence
Worden et al., JGR, 2011

## Slide 21: Spectral Anisotropy Estimate
R = anisotropy, F = flux, L = radiance, q=nadir angle, n=frequency
(assumes azimuthal symmetry)
Let x = sinq, then dx = cosqdq
using Gaussian integration of moments. From Abramowitz & Stegun
for n=1, k=1: xi = 0.666667 and wi = 0.50