## Slide 1: Validation of the CrIS-NH3 Retrieval with ground-based FTIR
Enrico Dammers, Mark Shephard, Shailesh Kharol, Chris McLinden
enrico.dammers@canada.ca

## Slide 2: Why use satellite observed NH3
NH3 total budget and distribution? Relatively uncertain…(Sutton et al., 2013)
Sparse distribution of measurements (Van Damme et al., 2015)
Hard to measure/ expensive measurements/ artefacts (Bobrutzki et al., 2010)
Satellite products(CrIS, IASI, TES):
    Global coverage
    Bi-daily measurements
    Real time monitoring
    Validation…..
      Often new versions (“research products”)… aka… (slightly) outdated validation studies
New goal:
  Frequently update the FTIR-NH3 as well as g-b in situ datasets & continuously extend the set with new locations
  Frequently evaluate and validate current satellite NH3 products
Yes ! this means I will once again bother you all with retrieval requests!

## Slide 3: CrIS-NH3
CrIS-NH3:
  Fast Physical Retrieval (Shephard and Cady-Pereira, 2015)
  Optimal Estimation
  Current product & start: v1.4 (beta) & 2013 - ..
  Data available on request (@:enrico.dammers@canada.ca, mark.shephard@canada.ca)
  Expected time needed for all retrievals: ~6 months

## Slide 4: CrIS-NH3
AMON IL37 Station

## Slide 5: Datasets - FTIR
FTIR – NH3 dataset (Dammers et al., 2015, ACP)
  Two spectral windows (931 & 967 cm-1) (slight differences for arctic & low conc sites)
  Interfering species: H2O, O3, CO2, N2O, HNO3, SF6, CFC-12, solar lines
  Spectra from NDACC FTIR sites
  Current set: nine sites
    High to medium: Bremen / Toronto / Pasadena / Mexico City
    Medium to low: Lauder / Boulder / Wollongong
    Low to arctic background: Thule / Eureka

## Slide 6: Datasets
Continued..
Where is my site!:
  Jungfraujoch & Maido: currently no “hits” with elevation criteria
  Tsukuba: no hits with current dataset
  Spitsbergen  Quick look in the past: no NH3 (potentially revisit dataset)
  Arrival Heights  Quick look: no NH3
  Paris: requested data, awaiting publication of dataset
  Campaigns: only used long term datasets
  Others, contact me! (enrico.dammers@canada.ca)

## Slide 7: Method
CrIS data filters:
  DOF ≥ 0.1
  Retrieved profile: ≤ 200ppb
  Cloud cover: Implicit by DOF filter
Collocation criteria:
  Temporal: ≤ 90 min
  Spatial: ≤ 50 km
Elevation:
  At no point between observations: Hdiff ≤ 300 m

## Slide 8: Results
CrIS-NH3 v1.3
Dammers et al., 2017

## Slide 9: Results
CrIS-NH3 v1.3
Dammers et al., 2017

## Slide 10: Results
CrIS-NH3 v1.3
Difference CrIS-FTIR
CrIS: Measurement error
FTIR – random error
FTIR – systematic
error
Dammers et al., 2017

## Slide 11: Recent developments
CrIS-NH3 v1.4 (beta)
  Improved a-priori
  Updated “improved” meteorology
  Streamlined retrieval
  “Bug fixes”

## Slide 12: Results
CrIS-NH3 v1.4 beta

## Slide 13
IASI
CrIS
Results

## Slide 14
Results

## Slide 15: Results

## Slide 16
Results

## Slide 17: Outlook
Call for updates of the FTIR-NH3 dataset
Validation of IASI-NNv2.1 (and further updates) (IASI-A and IASI-B)
Operational mode CrIS-NH3-v1.4

## Slide 18: Thank you for your attention!
And many thanks for the NH3 data provided by:
Mathias Palm, Erik Lutsch, Kim Strong, Jim Hannigan, Ivan Ortega, Geoff Toon, Nicholas Jones, Dan Smale, Corinne Vigouroux, Geoffrey C. Toon, Hideaki Nakajima, Isamu Morino, Beatriz Herrera, Wolfgang Stremme, Michel Grutter
enrico.dammers@canada.ca