## Slide 1: SFit2 Updates for 2013

## Slide 2
Two foci of sfit4 Development
  Sa (Sa-1) definition / direct input
  Background parameters (slope, curvature, zero)
  Shifts, by species, by fit
  Channeling
  SNR by region
  Multiple regions / SZA
  Fit gas by region
  Phase, ME
  Isotope separation
  Solar background /shift
  Levenberg-Marquardt non-linear iteration scheme
  Emission spectra
  Log(vmr) retrieval
  Line mixing (co2, ch4 soon…)
  SDV speed dependent Voigt lineshape
  Spectra output by layer / gas
  O2 CIA line data included
Process & I/O Speed – NDACC operational processing
  Standard layering
  Binary HITRAN input
  Binary output for HDF
Flexibility – Exploratory analysis tool

## Slide 3
sfit4
raytracing
retrieval
sfit4.ctl
Retrieval specific params:
Region
Species
State vector
t15asc4
Spectrum specific params:
Date/Time
Solar zenith angle
N spectra
stations.layers
Layering for each site
From WACCM
reference.prf
Z-p-T for reference profiles
Reference (apriori) chemical profiles
Binary (HITRAN) Line list file
detail
Step-by-step of retrieval process
statevec
Xa & X̂
K.Out
K matrix
Sε-1
Sa, Sa-1, Ŝ
pbpfile
Obs spectrum
Fitted
Difference
required inputs
basic outputs

## Slide 4
! --- SET DEFAULT FILENAMES
TFILE(08) = 'pbpfile'
! --- ISOTOPE SEPARATION FILE
TFILE(09) = 'isotope.input'
TFILE(15) = 't15asc'
TFILE(16) = 'detail'
! --- STATEVEC
TFILE(18) = 'statevec'
! --- SET MIXOUTPUT FILENAME AS STATE VECTOR FILENAME + .MXF
TFILE(17) = TRIM(TFILE(18))//'.mxf'
! --- SAVED SYNTHETIC SPECTRUM
TFILE(19) = 'synspec.out'
! --- SUMMARY
TFILE(20) = 'summary'
! --- SET PARTICAL COLUMN OUTPUT FILENAME AS STATE VECTOR FILENAME + .PRC
TFILE(22) = TRIM(TFILE(18))//'.prc'
! --- EMPIRICAL MODULATION FUNCTION
TFILE(23) = 'ils.dat'
! --- EMPIRICAL PHASE FUNCTION
TFILE(24) = 'ils.dat'
! --- CHANNEL OUTPUT
TFILE(30) = 'chnspec.data1'
TFILE(40) = 'chnspec.data2'
! --- SET SHORT FILENAME AS SUMMARY FILENAME + .ST
TFILE(31) = TRIM(TFILE(20))//'.st'
! --- DEFAULT FIRST RETRIEVAL GAS SA OUTPUT FILENAME
! --- OUTPUT DEPENDS ON NAME SA .NORM, .VMR, .PCOL
TFILE(61) = 'Sa.norm'
! --- DEFAULT SAINV INPUT FILENAME
TFILE(62) = 'Sainv.input'
! --- DEFAULT COMPLETE SA OUTPUT FILENAME
TFILE(63) = 'Sa.complete'
! --- DEFAULT K,SE,SA MATRICES OUTPUT FILENAME
TFILE(66) = 'K.out'
! --- SE OUTPUT
TFILE(67) = 'Se.out'
! --- DEFAULT K TRANSPOSED FILENAME
TFILE(68) = 'KT.out'
! --- LEVENBERG-MARQUARDT DETAILS
TFILE(70) = 'detail.opt'
! --- LAYERING SCHEME - OUTPUT FROM WACCM PROFILES
TFILE(71) = 'station.layers'
! --- REFERENCE VMR PROFILES
TFILE(72) = 'reference.prf'
! --- RAYTRACE DETAILED OUTPUT AKA TAPE6
TFILE(73) = 'raytrace.out'
TFILE(74) = 'raytrace.pt'
TFILE(75) = 'raytrace.ms'
TFILE(76) = 'raytrace.mix'
TFILE(77) = 'raytrace.sa'
TFILE(78) = 'raytrace.pnch'
! --- RESERVED FOR GASOUT NAME CHANGES - SEE FRWDMDL.F90
!TFILE(80)
TFILE(81) = 'AK.out'
TFILE(82) = 'SM.out'
TFILE(83) = 'SS.out'
TFILE(84) = 'A-S.out'
TFILE(85) = 'AEIGEN.out'
TFILE(88) = 'PRFS.out'
TFILE(89) = 'Parm.out'
TFILE(91) = 'Spec.out’
map of Input & output files … needs to be cleaned up

## Slide 6: outputs
Levenberg-Marquardt detailed output
Raytrace detailed output
Raytrace summary output
Raytrace output in sfit2 input form (pt, ms & mix format files)
Raytrace layer-based Sa models
Spectra by gas or spectra by gas and iteration
Channel spectra
Synthetic spectra
Averaging kernels
Averaging kernel eigenvectors
Measurement error covariance
Smoothing error covariance
Retrieved profiles
Statevector by iteration
Final mixing ratios
Final partial columns
Sa output
Summary (short) output
Binary output (X, X̂ , K, Sa, Se, Sa-1, convergence, iteration, RMS)
New
Debugging
Remove

## Slide 7: new HITRAN data input scheme
001_H2O:
01_hit08.par
01_hit08.zip
01_hit09.par
01.H2O
002_CO2:
02_hit08_f53.par
02_hit08_f53+LM.par
02_hit08.zip
02.CO2
co2_lm.dat
read_out_example.txt
.
.
.
Predefined directory structure:
Stand alone code hbin.f90 compiled with sfit4 is run before sfit4 call.
hbin* reads files:
  sfit4.ctl
  hbin.input
  isotope.input
  Hitran files directly
Writes file: lllll.dddddd-hhhhh.dddddd.hbin
Sorts all lines in wavenumber order, edits id numbers, separates isotopes, can choose gases and adds flags for:
  CIA
  line mixing parameters
  Galatry parameters
  SVD parameters
hbin is run once for a specified retrieval
See: docs/hbin_descrip_v4.docx

## Slide 8: (slightly) new isotope separation input scheme
See: docs/isotope_descrip_v4.docx
Main differences:
  Profile for new gas is now on pre-raytrace or ‘refmod’ grid
  There are no default pre-separated species
  You can add subsequent isotopes to the new species that will use the new profile eg.
    H2O 1/4 -> HDO 80/1 (HD16O)
    H2O 1/5 -> HDO 80/2 (HD18O)
    H2O 1/6 -> HDO 80/3 (HD17))

## Slide 9
(slightly) new ascii spectral data file
37.26100 6385.44500 40.03800 254.76000
2011 6 23 16 24 11
06/23/2011 16:24:11UT Z:37.261 A:284.29 D:0101.7 R:0.0035 P:BX F:01.9139mr
4881.8975000000000 4888.1025000000000 2.50000000000000005E-003 2483
0.315438E+00
0.293434E+00
0.285126E+00
0.271612E+00
0.240477E+00
.
.
.
header for each block:
KEY:
SZA° radius_of_earth [km] latitude [°N] longitude [°E]
YYYY MM DD HH MM SS
arbitrary ascii comment 80 characters
start_wn end_wn point_spacing Npoints
spectra values…
Any number of blocks are ok
All blocks with spectra within sfit4.ctl band limits will be fit
Spectra will be truncated to sfit4.ctl band limits

## Slide 10
# General
file.stalayers = station.layers
file.refprofile = reference.prf
file.spectrum = t15asc.4
file.eap_dat = ils.dat
file.ephs_dat = ils.dat
file.sa_matrix = sa.input
file.isotope = isotope.input
file.solarlines = ..//linelist/solar/120621/solar.dat
file.linelist = ./02723.690800-02930.039200.hbin
# Definition for retrieval gases
gas.layers = 47
gas = HCL CH4 O3 HDO N2O NO2
gas.HCL.ifoff = 1
gas.HCL.zwid = 3.000
gas.HCL.zmin = 0.225
gas.HCL.zmax = 120.000
gas.HCL.logstate = F
gas.HCL.ifprf = T
gas.HCL.sigma =
0.62398 0.33613 0.33382 0.22898 0.14726
0.14435 0.14265 0.14204 0.14226 0.14383
0.14538 0.14531 0.14490 0.14430 0.14320
0.14272 0.14354 0.14652 0.15191 0.15851
0.16395 0.16691 0.17080 0.17993 0.19615
0.21887 0.24784 0.27969 0.30479 0.32309
0.34501 0.37861 0.42903 0.50225 0.58601
0.62527 0.61862 0.63071 0.73872 0.92782
1.08104 1.19786 1.28879 1.35951 1.42124
1.46301 1.48165
gas.CH4.ifprf = F
gas.CH4.sigma =
1.00000 1.00000
# Forward model parameters
fw.delnu = 0.10000
fw.lshapemodel = 0
fw.linemixing = T
fw.linemixing.gas = CO2
fw.solar = T
fw.solar.shift = 0.00000
fw.ifps = F
fw.ieap = 4
fw.neap = 0
fw.iephs = 4
fw.nephs = 0
fw.emission = F
fw.ifiso = T
fw.write_k = T
fw.write_gasfiles = T
fw.write_gasfiles.type = 1
(Very new) sfit4.ctl
General I/O files
Retrieval Gases
Forward Model Parameters

## Slide 11
# Retrieval parameter
rt = T
rt.write_sa = F
rt.lm = F
rt.lm.gamma_start = 100000.
rt.lm.gamma_dec = 10.0
rt.lm.gamma_inc = 10.0
rt.convergence = 0.1
rt.tolerance = 0.05
rt.max_iteration = 15
rt.wshift = 2
rt.wshift.apriori = 0.000
rt.wshift.sa = 0.100
rt.slope = T
rt.slope.apriori = 0.000
rt.slope.sa = 0.100
rt.solar = T
rt.solar.apriori = 1.000
rt.solar.sa = 0.500
rt.ifdiff = T
rt.temperature = F
rt.raytonly = F
# Microwindows and their parameters
band = 1 2
band.1.nu_start = 2727.730
band.1.nu_stop = 2727.830
band.1.zshift = 0
band.1.zshift.apriori = 0.000
band.1.zshift.sa = 0.200
band.1.beam = 0
band.1.dn = 0.800E-03
band.1.wavfac = 1.000
band.1.pmax = 257.143
band.1.omega = 2.273
band.1.iap = 0
band.1.snr = 200.000
band.1.gasb = HCL O3 HDO
band.2.nu_start = 2775.700
band.2.nu_stop = 2775.800
band.2.zshift = 0
band.2.zshift.apriori = 0.000
band.2.zshift.sa = 0.200
band.2.beam = 0
band.2.dn = 0.800E-03
band.2.wavfac = 1.000
band.2.pmax = 257.143
band.2.omega = 2.273
band.2.iap = 0
band.2.snr = 200.000
band.2.gasb = HCL O3 N2O
Retrieval parameters
Band Parameters
# Retrieval parameter
rt = T
rt.write_sa = F
rt.lm = F
rt.lm.gamma_start = 100000.
rt.lm.gamma_dec = 10.0
rt.lm.gamma_inc = 10.0
rt.convergence = 0.1
rt.tolerance = 0.05
rt.max_iteration = 15
rt.wshift = 2
rt.wshift.apriori = 0.000
rt.wshift.sa = 0.100
rt.slope = T
rt.slope.apriori = 0.000
rt.slope.sa = 0.100
rt.solar = T
rt.solar.apriori = 1.000
rt.solar.sa = 0.500
rt.ifdiff = T
rt.temperature = F
rt.raytonly = F
# Microwindows and their parameters
band = 1 2
band.1.nu_start = 2727.730
band.1.nu_stop = 2727.830
band.1.zshift = 0
band.1.zshift.apriori = 0.000
band.1.zshift.sa = 0.200
band.1.beam = 0
band.1.dn = 0.800E-03
band.1.wavfac = 1.000
band.1.pmax = 257.143
band.1.omega = 2.273
band.1.iap = 0
band.1.snr = 200.000
band.1.gasb = HCL O3 HDO
band.2.nu_start = 2775.700
band.2.nu_stop = 2775.800
band.2.zshift = 0
band.2.zshift.apriori = 0.000
band.2.zshift.sa = 0.200
band.2.beam = 0
band.2.dn = 0.800E-03
band.2.wavfac = 1.000
band.2.pmax = 257.143
band.2.omega = 2.273
band.2.iap = 0
band.2.snr = 200.000
band.2.gasb = HCL O3 N2O