## Slide 1: Retrievals at U of T: Toronto and Eureka Stations
Cyndi Whaley, Camille Viatte, Stephanie Conway, Pierre Fogal, Kimberly Strong
November 14th 2012
Input for IRWG-NORS Workshop

## Slide 2: Overview
We use a bit of everything
  Matlab and DOS executables to prepare files
  Fortran90 and C codes for retrievals
  IDL codes for error analysis
  IDL and Matlab codes for plotting results
  Python codes or linux commands for creating files list and bash scripts to run batches of files
Procedures vary slightly between the two sites…

## Slide 3: Species Currently Archived on the NDACC Database
Eureka:
Toronto
Archived in NASA Ames format (archived data uses old a priori profiles, not WACCM and not necessarily the IRWG-recommended microwindows)
Plan to move to HDF with full reproccessing of both datasets
*We have acquired all Eureka Bomem DA8 spectra from Environment Canada and have begun to reanalyze with SFIT2/4 using the same retrieval parameters as used for the Eureka Bruker 125HR (Pierre)
Total and Partial Columns: CH4, CO, ClONO2, HCl, HF, HNO3, N2O, O3 | Bruker 125HR | 2006 - 2011
Total colums: HCl, HF, CH4, N2O, O3, HNO3, ClONO2, NO, NO2, ClO, COF2 (analyzed with SFIT1 by Hans Fast) | *Bomem DA8 | 1996-2006
Total and Partial Columns: CH4, HCl, HF, N2O, NO, NO2, O3 | Bomem DA8 | 2001 - 2009

## Slide 4: Work in Progress
We have done a lot of work implementing and testing the retrieval parameters recommended by the IRWG:
Eureka:
  CO, C2H6, HCN, CH4, and O3 retrieved for all years with IRWG microwindows and WACCM a priori information, and error analysis performed (Camille)
  HCl, HNO3, HF, ClONO2, and N2O retrieved for 1 year without error analysis to evaluate the new strategy (Rodica)
Toronto:
  N2O, CO, C2H6, CH4, O3, HCl, and HF retrieved for all years with IRWG microwindows and WACCM a priori information, and error analysis performed (Cyndi)
  HCN retrieved with new strategy (different a priori profile and different 3rd MW) for all years without error analysis (Cyndi)
Need to complete reanalysis of datasets, convert to HDF and archive

## Slide 5: File Conversion for Spectra
Eureka:
  For 125HR: IDL functions and DOS executables* to convert OPUS format spectra (.0, .1, …) to a binary file (.BNR) and metadata file (.mdb)
  For DA8 historical dataset: have new python2 program (spc_convert2.py) to read the binary GRAMS .SPC files. Testing the option to read older labcalc .SPC files
Toronto:
  Matlab functions & DOS executables* to convert Bomem DA8 files (.SPC) to binary files (.BNR) and calculate SZAs
  *sun_moon.exe, specinfo.exe, opu2sfit.exe
  Note: these executables only work on 32-bit computers. We have not been able to run the spectral conversion on 64-bit computers.

## Slide 6: Temperature and Pressure
Eureka
  Linear interpolation of radiosondes for z < 35 km
  NCEP (everyday at noon) for 35 km < z < 50 km: reformatted with IDL code create_ncep.pro
  MSIS (Mass Spectrometer Incoherent Scatter radar extended modes solar activity index) used for z > 50 km
  All meteorological data combined together using three MATLAB codes:
  - CreateZPT_205_to61L_Becs.m
  - CreateZPT_Becs.m
  - CreateZPT_finalsub_Becs.m
Toronto
  Goddard Automailer to get the Toronto temperature and pressure from NCEP and Matlab function (makezpt_v2.m) to add WACCM T and P for z > 50 km, and convert to zpt files.

## Slide 7: Zephyr2
Zephyr2 to organize and automate SFIT2 v3.94 analysis and internally runs fitman2, based on fitman by Paul Johnson

## Slide 10: Batch Runs
Use python script to generate bash file
Or use pre-generated file lists (generated with LINUX command at the time of conversion to bnr file) to create bash file
Change mode to make file executable and run script in “screen” mode
Example bash script:
------------------------------------------------------------------------------------
#!/bin/bash
zephyr2 zinput-o3 070304X2.S02.bnr
zephyr2 zinput-o3 070304X2.S17.bnr
zephyr2 zinput-o3 070304X2.S29.bnr
zephyr2 zinput-o3 070304X2.S44.bnr

## Slide 11: Output and Plotting
Outputs: profiles, K, fits, averaging kernels…
Plotting:
  IDL plots : profiles and spectral fits (sfit2plt.pro)
  IDL program to summarizes in a single binary file all important information and produces a .sav file ** (sfit2rdz.pro)
  Use output .sav file to create ASCII files, which we use to produce plots with MATLAB
  ** This is where we apply the quality filter on retrievals. Should this be done before analyzing all the spectra?

## Slide 12: Error Analysis
Use IDL functions to perturb parameters and zephyr2 to run sfit2
Manually perturb SZA
awchcfgl.pro multiplies air broadened half width by 1.05
changecfgl.pro multiplies line intensity by 1.05
singleparameter.pro creates K vector for SZA, line width and line intensity
doptpert.pro perturbs the temperature of each layer individually by 2 K to determine the impact on the overall retrieval
errorcalc.pro calculates the error

## Slide 13: Error Analysis
The error analysis is run on a representative dataset of spectra : about 10 spectra (of varying SZA, season, time of day and year) per species, and that average percent error is applied to the whole time series
List of errors summarize in this Table
Sm(%) | measurement error
Ss(%) | smoothing error
Stemp(%) | uncertainty on temperature
Slineintens(%) | uncertainty on line intensity
Slinewidth(%) | uncertainty on line width
Sint1 (%) | uncertainty on retrieval parameters
ret params | 
Sint2 (%) | uncertainty on interfering species
intf. spec. | 
SSZA (%) | uncertainty on SZA
Stot (%) | total random error
random | 
Stot (%) | total random and spectral error
rand+spectr | 
Stot(%) | total error
DOFS | Degrees of Freedom

## Slide 14: Future Work / Needs
Need to improve/change
  Flag to calculate (or not) error budget for each retrieval
    Feasible?
    Not with perturbation method?
    Comparable to PROFITT
  Error processing still requires too much manual effort/intervention
  Ability to convert spectra and calculate SZA on 64-bit computers
  Code to pre-filter spectra?
Would like to improve/change (currently working on)
  Archiving in HDF format
New Requirements
  Kb for error components for each retrieval
    Probably at fit-time & stored with standard fit output
    Or parameterized?
  Batching for error calculations & HDF build