## Slide 1
Relies on a mixture of fortran, idl and a few minor shell scripts (bash)
  Both windows (post-processing) and unix (sfit2) based
  Uses unix cluster with simple scripts to run on 1 to n cpu’s (most so far 50)
Uses FORTRAN codes from GFIT to prepare spectral run
  Create_sunrun_from_Wgong.f90 / create_runlog.f90
    Calculates SZA, radius of earth, FOV … and produces housekeeping file
  Fitb302.f90 – main code wrapper for sfit
    Reads runlog, runs fastcode, updates all input files, baseline corrects, reduces resolution, zerofills, zero corrects, reads OPUS format files on the fly to create temporary t15asc, calls sfit2 as subroutine call.
Uses IDL
  Plotting (splt392, plotpbp)
  Collates all output files from fitb302 run (nwrdsfit2394), creates idl binary data file structure
  Computes averages, seasonal cycles, bootstrap resampling, trend analysis, statistics, and various sorting criteria to remove bad fits, ascii O/P for HDF (gas394)
  All error codes (NCAR codes from Jim)
    Perturbation codes dspec, dpoint…
    Errorcalc – combines perturbation output with each retrieval data structure
Existing Wollongong Retrieval Processing

## Slide 2
Spectra measured and controlled by Spectronus
  OPUS spectra and csv log files
  Store in a directory by day (yyyymmdd)
  Code: visual basic, (c and fortran libraries), OPUS
Check OPUS data visually after each daily run
  Run cleanup.f90, removes bad spectra based on the tracker quad detector signals stored in csv logfile as cloud filter
  Run quickly through spectra using OPUS quick view to check selected spectra
  Run extract OPUS_MIR an OPUS macro to save spectra blocks only
  Code: Fortran, OPUS macros
System level pre-processing
  Archive data (interferograms +spectra) to mass storage system
  Store spectra blocks on local storage for analysis
  Code: Winscp
Create listing of spectra using GGG programme suite
  Creates runlog with spectra name, date, time, lat long, snr, SZA, AZM, Duration…
  Code: fortran
Process outline through to fit of a gas 1/2

## Slide 3
Create z-p-t-w profiles for day
  Download NCEP p T z w from noaa, store in nc files
  Extract z p T w data into refmod formatted in <daydir>
  Use mean standard WACCM profile from monthly mean profiles
  Code: IDL, netcdf, FORTRAN
Run sfit from spectra list for specific gas using fitb302
  Cinput control for fitb302 contains gas ID, location and file with altitude grid for fastcode, location of met files and refmod files (daily/averaged refmod files controlled by switches), working directories for workspace and spectra, also various controls for spectral file type (read bnr, native opus, bomem spc), unix/windows file types, multiple run options for prefitting gases, signal to noise calculations, resolution reductions, and other fitting options
  On Unix cluster, split runlog into equal size (300-500), create individual gas fitting subdirectories, submit each job to queue (anything from 1 to 50+ cpus)
  Collate all sfit2 output files (via tarball) onto local pc
  Code: FORTRAN, shell scripts (PBS)
View outputs
  Plot a single retrieval: fits, vmrs, K matrix, AK’s etc
  Code: IDL (splt392)
Process outline through to fit of a gas 2/2

## Slide 4
Untar files from previous run
  Create output directory, compile sfit files in a data directory, fastcode files into a clim directory, and concantonate an output runlog file (spectra, date, time, columns, rms fits, etc)
  Nwrd.ctl control file for nwrdsfit2392.pro
  Control file contains working directories, binput file, fastcode directory (ms, pt, mx), number of partial columns and their boundaries, interval to computer signal strength ratio (ssr), output runlog file, and various switches to control format types of files and code versions etc.
  Create idl binary sav file
  Code: IDL
Compute gas products (daily means and stats) including data for archiving
  Gas.ctl control file: number of idl sav files (can combine several sav files from different gases), year range, sfit2 version, selection criteria for rms and ssr, metrics for retrieved profile stability, systematic and random errors for all partial column layers (based on results from separate error assessments)
  Create structure use selected spectra to compute daily/monthly means and their errors, trends using nonlinear gradient expansion fits, boot strap resampling on error statistics to confirm their robustness, correlation matrices, averaging kernels, ascii outputs for various programmes (HDF, envisat, research papers etc).
  Code: idl (gas394.pro)
Post-Processing