## Slide 1
Relies heavily on shell scripts (korn)
  Always has been unix based
  Uses standard utilities: sed, tr, head, tail, grep…
  Uses nested scripts :
    run 1 retrieval to multiple years & gases with same scripts & naming conventions
Uses C & FORTRAN codes to prep spectra
  ckopus.c – converts opus to .bnr (simple intermediate binary spectra file)
    Calculates SZA, radius of earth, FOV …
  specasc6.f90 – converts .bnr to t15asc (for sfit)
    Ratio with filter envelope, baseline correct, reduce resolution, zerofill
  coad.c – averages multiple .bnr files
Uses IDL
  Plotting (oex, cprf…)
  All error codes
    Perturbation codes dspec, dpoint…
    Errorcalc – combines perturbation output with each retrieval data structure
    Idlcr8hdf from AVDC
Existing NCAR Retrieval Processing for MLO & TAB at a Glance

## Slide 2
Need to improve/change
  Require error calculation for each retrieval
  Error processing still requires too much manual effort/intervention
Would like to improve/change
  Like to not build input for idlcr8hfd
    Incorporate into errorcalc program?
    Or new program…
We like the flexibility and simplicity of scripts
  Would not move to compiled code, IDL or Matlab for batching
  Would consider using python
New Requirements
  Kb for error components for each retrieval
    Probably at fit-time & stored with standard fit output
    Or parameterized?
  Batching for error calculations & HDF build
Limitations / Needs / Keep / Toss

## Slide 3
Download data to local server (every week or 2)
  This is OPUS data, housekeeping files (eg. wx data) and log files
  Store in a directory by day (yyyymmdd/ or referred as a daydir) (this is an intermediate stop)
  Code: shell script using wget or rsync
Check OPUS data visually (intermittent but by month max)
  Delete bad spectra (typically bad baseline, excess noise, clouds…)
  Code: IDL, C : read, plot & delete opus files quickly
System level pre-processing (intermittent but by month max)
  Archive data to mass storage system
  Change filenames (lower case…)
  Set permissions (can get messed up in ftp process)
  Copy to working directory – new directory of <daydirs> with only good spectra
  Code: shell scripts
Create listing of spectra (several months or year!)
  Output 1 : spectra.YY.list - date, time, bandpass, snr, SZA, AZM, Duration…
  Output 2 : slist.YY – directory path to data, filename, opus data block, UTC offset
  Code: shell script, C
Process Outline Through to Fit of a Gas 1/2

## Slide 4
Create z-p-t-w profiles for day (several months or year!)
  Extract surface p, T, w from house-keeping file (TAB) or site archive (CMDL (MLO) or EOL (FL0))
  Download NCEP p T z from ndacc.org (or automailer)
  Interpolate NCEP data and spline in WACCM monthly mean p & T above
  Store refmod formatted z-p-T-w file in <daydir>
  Create WACCM refmod formatted water profile from monthly mean profiles
  Code: IDL, netcdf, FORTRAN, shell scripts
Run sfit from spectra list & gas.region list files (several months or year!)
  Spectra list (slist.YY) has spectrum type, location of opus file, opus data block, UTC time offset…
  Gas.region list (rlist) list has output directive, location of binput, fit spectral region, filter #
  Site directory (mlo) has WACCM profiles (refmod), ILS.dat, fastcode template
  Output saved to <daydir>/<gas.region>/<obstime> (all sfit output + all inputs to run again)
  Rslt.l : location of output, date, time, SZA, column, snr, fitrms, …
  Rslt.q : location of output, date, time, SZA, column, snr, fitrms, vmr(1:nlayers) …
  Rslt.qc : location of output, date, time, SZA, column, snr, fitrms,partial_columns(1:nlayers) …
  Code: shell script, C, FORTRAN
View outputs
  Plot a single retrieval: fits, vmrs, K matrix, AK’s etc
  Plot time series of eg 1 or many years
  Code: IDL
Process Outline Through to Fit of a Gas 2/2

## Slide 5
Day Directory
YYYYMMDD
House.log
Macro.log
Dispatch.log
Opus_f1.001
Opus_f2.001
Opus_f3.001
.
.
.
Zpt.refmod
H2o.refmod.v01
Spectra List (eg. slist.YY)
OPUS
FIT /p/ya4/wd/mlo/20100103/ SNGC s1ifmb1d.0 0
FIT /p/ya4/wd/mlo/20100103/ SNGC s1ifmb1d.1 0
COAD /p/ya4/wd/mlo/20100103/ 2 SNGC s2ifmb1d.0 0 s2ifmb1d.1 0
.
.
.
END
SDIREC
o3.1005 6
hcooh.1100 9
h2o.2938 3
co2.2492 4
hf.4038 2
END
Gas.Region List
WACCM profiles in REFMOD format
ILS data files
Filter envelope spectral files
Fastcode template file
Station.layers file
WACCM water vapor monthly averages
Spectral list files
Site Directory
File / Directory Components Used in Batch Retrieval Process
Binput.3.92
Binput.3.94
Binput.test
.
.
.
Gas.Region Directory
(eg. O3.1005)

## Slide 6
fitbn
Spectra List
slist.yy
Gas.Region List
rlist
Spec in region?
Convert to bnr
Get binput template
Get fastcode template
Create fitone.input
Call fitone.k
Save all output to<daydir>/<gas.region>/<utctime>
Another gas.region?
Another spectra?
yes
get another gas.region
Rslt.l
Rslt.q
Rslt.qc
Output lists:
Fit details
VMR
Partial Col
Flow of Batch Retrieval Process
yes
Done
yes
no
no
DayDir/Gas.Region/UTCTime
All input & All Output
For this retrieval
# of spectra in slist.yy * # regions in rlist = # retrievals
# regions (gases) is arbitrary
Summary of output saved to lists:
Fitone.k:
Make fastcode inputs & Call fastc.k
Make binput & call sfit2.k
Grab sfit output to make list files
Excluding fitalot…

## Slide 7
sfit2
fastcode
sfit2.k
Expects all files
Calls specasc6
Calls sfit2
specasc6
fastcnvert
fastc.k
Checks input
Calls fastcode
Calls fastconvert
Re-Names output
fitn.k
Edits input files
Calls fastc.k
Calls sfit2.k
fitbn
Gathers spectra
Gets binput template
Gets atmos. model
Writes fitone.inp
Calls fitn.k
Saves output
fitone.inp
Slist.YY
rlist
Nested Scripts for Calling Spectra Process & Fitting Codes
fitalot
Send multiple slists to fitbn
flist
Fit many years/gases
Fit one year/many gases
Create fastcode & sfit2 inputs for one spectrum/gas/sza
Raytrace for one atmosphere/sza
Make T15 & fit one spectra/gas/sza

## Slide 8
Create intermediate archive file for eg. 1 year of retrievals
  From sfit output: to <daydir>/<gas.region>/<obstime>/* collect all apriori, & retrieved, ancillary data needed for HDF file
  Read from Rslt.l list of retrieval directories
  Sort by fit criteria eg. RMSFIT, CONVERGENCE etc.
  Good data stored in array of IDL structures in ’.sav’ file
  Code: IDL
Determine errors for a typical test-case for this gas
  Create Kb for all uncertainties (line strength, pointing etc) use perturbation and repeated calls to sfit on this test-case
  Error components: air broadened half width, line intensity, pointing, ils modulation/phase, temperature profile, Interferences: slope, curvature, shifts
  Save Sys.covariance and Ran.covariance & column uncertainties for this gas
  Code: IDL
Make HDF for 1 gas, 1 year
  Read in .sav, *.covariance, metadata, table.data
  Build input for idlcr8hdf
  Run idlcr8hdf an make an hdf file
  Code: IDL
Process outline after fit to HDF Archive file 1/2

## Slide 9
Test case
1 per gas
Binput
K.Mat
Spectra
State vector
.
.
.
Dspec.pro
Perturbation:
Line Intens
A_b ½ width
Kb.lwidth.cov
Kb.lstren.cov
∂Fb/∂x
Dlshape.pro
Perturbation:
Modulation eff
Kb.ils.cov
∂Fb/∂x
Dphase.pro
Perturbation:
Phase fcn
Kb.phase.cov
∂Fb/∂x
Dtemp.pro
Perturbation:
Temperature
Kb.temp.cov
∂Fb/∂x
Dpoint.pro
Perturbation:
Solar ZA
Kb.point.cov
∂Fb/∂x
ErrorCalc.pro
For HDF:
Ran.covariance
Sys.covariance
Col_Ran.err
Col_Sys.err
+ individual error components
Creation of Error Matricies & HDF File
Perform separate calculations of component sensitivities by repeated calls to sfit2. Combine these into the covariance matricies for the HDF file.

## Slide 10
For this Gas:
Mygas.sav
  Timeseries of retrieval data structures
Ran.covariance
Sys.covariance
Col_Ran.err
Col_Sys.err
Makehdfdata.pro
Gas.year.Hdf.input
tableattrvalue_03R005_idl.dat
molec_mdata.meta
Idlcr8hdf.pro
groundbased_ftir.o3_ncar002_mauna.loa.hi_19950827t163411z_19951230t175759z_001.hdf
HDF Archive Process: After retrievals to HDF