## Slide 1: Long open path Fourier transform spectroscopy measurements of greenhouse gases in the Near-IR
David Griffith
University of Wollongong, Australia
&
Denis Pöhler, Stefan Schmitt, Sam Hammer, Sanam Vardag, Ingeborg Levin, and Ulrich Platt
University of Heidelberg, Germany
TCCON/NDACC Toronto June 2015

## Slide 2: History: open path FTIR – mid IR Measuring greenhouse gases from agriculture
Tracer release (N2O)
FTIR beam
wind
FTIR
Retroreflector
FTIR & telescope

## Slide 3: OP-FTIR-tracer: results

## Slide 4: Because we are in Canada… Alberta 2013

## Slide 5: FTIR meets DOAS in the NIR
Accurate greenhouse gas measurements are mostly point-based
  Using calibrated in situ analysers
  Or flask samples
Open path spectroscopy has some advantages
  Spatial averaging, better match to regional-scale model resolution
    How spatially representative are point measurements?
    How accurate are open path measurements?
We know that TCCON provides precise measurements of GHGs:
  Solar absorption spectroscopy, 8-20 km-atm atmospheric path
How well can we measure GHGs at the ground in the NIR?
  Low resolution portable FTS
  Weaker source than the sun (50W quartz lamp)
  2-6 km path

## Slide 6: Long path FTS setup
FT
detector
interferogram
source
spectrum
FT
Interferometer
0.5 cm-1 resoln
Bruker IRcube
1-3 km
Illuminating bundle
Receiving fibre

30 cm
FL
150 cm
17 x 70mm
retroreflectors

## Slide 7
IUP
Retrorefl.

## Slide 9: FTIR-DOAS setup

## Slide 10: NIR long path spectrum 3.1 km return path IUP - Philosophen Weg
Weak CO2
Strong
CO2
2
1.6
Microns
1.25
2.5
CH4
O2
1.4
H2O
H2O

## Slide 11: “Strong” CO2 band 4900-5000 cm-1
CO2
H2O
CO2

## Slide 12: CH4 is weaker…
CH4

## Slide 13: O2
O2

## Slide 14: Spectrum analysis : MALT least squares fit CO2

## Slide 15: Spectrum analysis : O2

## Slide 16: ILS: short path H2O Fit H2O 7000-7400 cm-1 (Frey, Hase et al., AMTD 2015)
Hamming
Apodisation
ME ~ 0.7

## Slide 17: O2 and temperature

## Slide 18: O2 and temperature

## Slide 19: O2 and temperature
Mean O2 = 0.217 (+3.5%)

## Slide 20: CO2 – 3 days in July
Germany wins
World Cup!
Cal adjust 16.2 ppm

## Slide 21: CO2 4 months July-October 2014

## Slide 22: CH4 July-October 2014

## Slide 23: CO2 OP-in situ differences

## Slide 24: Summary: CO2 precision and accuracy
Precision/repeatability
  ~1 ppm (0.25%, 1s) for 5 min averages
    limited mainly by spectrum SNR
    300mm telescope, 17 retros, 50 W source
  ~ 40 ppm p-p differences to in situ measurements
    Real differences, larger at low wind speeds
Accuracy/bias
  ~3% uncalibrated (~ 13 ppm)
  Limited by
    HITRAN, simulation ~ 2-4%
    Temperature ~ 3C (1%)
    Pressure <1 hPa, (0.1%)
    Pathlength <3 m (0.1%)
    Fibre residual ~1%

## Slide 25: Now – the residuals …

## Slide 26: Co-fitting fibre residual DCO2 in retrieval <0.5 ppm

## Slide 27: An interesting artefact …
18:15 every sunny day!

## Slide 28
Solar beam travels through ~17 km path
- Apparent increase in CO2, CH4, O2

## Slide 29: Current setup
FT
detector
interferogram
source
spectrum
FT
Interferometer
0.5 cm-1 resoln
Bruker IRcube
1-3 km
Illuminating bundle
Receiving fibre

30 cm
FL
150 cm
17 x 70mm
retroreflectors

## Slide 30: A better setup
detector
interferogram
source
FT
interferometer
1-3 km
Stray and scattered radiation (eg sunlight) is not modulated, appears only as DC and does not appear in the FT spectrum

## Slide 31: Potential improvements & future work
Pre-modulate IR source before transmission
  Removes stray light
More photons
  Precision is detector noise limited
Remove or co-fit fibre spectral structures
Higher resolution?
  Better discrimination against fibre residuals
  Lower SNR => lower precision
  Less portable
Temperature measurement
  Improve retrieval

## Slide 32
Thank you !

## Slide 34: Some applications
Distributed measurements cf in situ point measurements
Validation of point measurements in inhomogeneous environment
Fluxes (conc * windspeed = flux)
  Eg cross-Neckar path, perpendicular windspeed
Fluxes – with backward Lagrangian model (eg. STILT, Windtrax)
Mass balance methods
  Paths surround source/sink, measure path concentrations and windspeed
Tracer studies
  Eg cattle CH4

## Slide 35: Co-fitting residuals
~80-90% of the variance in the residual is constant
  => due to the fibre
~1% of the residuals correlate with CO2 spectrum
  R2 (residual-CO2)= 0.01
Co-fitting fibre structure changes retrieved CO2 by < 1 ppm

## Slide 36: Co-fitting residuals
~90% of the variance in the residual is approx. constant
  => due to the fibre
~1% of the residuals correlate with CO2 spectrum
  R2 (residual-CO2)= 0.01
Co-fitting fibre structure changes retrieved CO2 by < 1 ppm
Residual after co-fitting fibre spectrum reduced but not white noise
  => better estimate of random uncertainty from the fit
Note: this method is also used in OCO-2 retrieval
More work required!!!