## Slide 1
Corinne Vigouroux, Omaira García, Jim Hannigan, Ivan Ortega, Yana Virolainen, Dan Smale, Michel Grutter, Isao Murata
+ all IRWG PIs measuring ozone, as data provider
+ volunteers for specific TOAR-II work ?
TOAR-II (Tropospheric Ozone Assessment Report)
FTIR contribution

## Slide 2: TOAR-I (2014-2019)
Fig. 4.3.1.2 of Gaudel et al., (2018)
FTIR participated in 2 papers:
Tarasick et al.: general FTIR description + error budget and comparisons with sondes from Omaira
Gaudel et al.: trends of tropospheric O3 at 8 FTIR sites with long-term measurements
Only for surface data
Other data sets (satellites, sondes,…): links to each individual database.
Leads: O. Cooper & M. Schultz

## Slide 3: TOAR-II (2020-2024) objectives
An up-to-date assessment of tropospheric ozone’s distribution and trends on regional, hemispheric and global scales.
Explore and quantify the impacts of tropospheric ozone on human health, crop and ecosystem productivity and climate change.
Two TOAR-II Special Issues:
  a set of papers contributing to the TOAR-II Community Special Issue:
- Paper topics developed through Focus Working Groups
- Any independent study that contributes to TOAR-II objectives and support the final TOAR-II assessment can be submitted in the TOAR-II special issue
  2) a set of core papers (including the assessment report) will be identified by the TOAR-II Steering Committee, based on input from the TOAR-II community
Leads: O. Cooper & M. Schultz

## Slide 4: Focus Working Groups
Chemical Reanalysis
East Asia
HEGIFTOM (Harmonization and Evaluation of Ground-Based Instruments for Free Tropospheric Ozone Measurements)
Ozone over the oceans
Ozone and Precursors in the Tropics (OPT)
Radiative Forcing
Satellite Ozone
Statistics
Tropospheric Ozone Precursors (TOP)
Urban Ozone
I’ve been contacted by WG leads to participate to HEGIFTOM and OPT (data collection; 0-8km with quality check and uncertainties; FTIR trend analysis).
Jim, Ivan / Omaira / Yana joined HEGIFTOM with platforms comparisons.
I contacted TOP to join with FTIR measurements. (HCHO, CO)
Michel joined OPT with Altzomoni data. Presentation in the next OPT meeting.
Everybody is free to join us in these 3 WGs.
But also other WGs: East Asia ? Urban ozone ?
WGs will work in close collaboration

## Slide 5: HEGIFTOM: Expected Outcomes
Homogenized time series of measured tropospheric ozone with uncertainty estimates and quality flags included.
Traceability to a common standard for the different ground-based networks
Characterization and eventual correction of instrumental drifts based on cross-comparisons between instruments at sites hosting different techniques.
Assessment of the tropospheric ozone distribution and trends of tropospheric ozone.
2021: Internal consistency within each network
2022: External consistency among the networks
2023: Preparation publication(s) and exploitation of data sets with other TOAR-II WG’s
Leads: R. Van Malderen & H. Smit

## Slide 6
  HEGIFTOM 2021: Internal consistency
  To be done:
    For TOAR-I, the uncertainty budget was not provided for all sites: we used 5% Random and 3% Systematic.
    Check/harmonize the current uncertainty consistency : random and systematic provided at each site? Harmonized values? For our next update: use the uncertainties defined in the IRWG common tools.
    The smoothing error - dominant for tropospheric column - has to be estimated at each site.
  Done:
    Homogenization: retrievals settings within NDACC still follows Vigouroux et al., ACP, 2015.
    Data collection from NDACC + RD + few stations not in NDACC yet : will be used for IGAC 2021 and QOS 2021.
    Quality flag: no flagging in our geoms files; Quality check was done « manually « by myself (e.g. few outliers removed; oscillating profiles reported to PIs, too high/low DOFS reported to PIs…)
    Uncertainty estimates: IRWG reports random & systematic components, in agreement with advise from TUNER work (von Clarmann et al.), this is appreciated and other techniques will try to follow.
Question for IRWG: While updating WACCM; spectroscopy versions;… should we also move towards an improvement of the strategy (4/5 mws; García et al., AMTD, 2021) ?

## Slide 7
  Inter-comparisons with other techniques at super sites:
    FTIR / sondes: done / started
        Jim & Ivan: Eureka, Boulder, Izaña, Mauna Loa, Lauder, Ny-Alesund
        Isao: Tsukuba
        Both: Interact and publish ? Present at next HEGIFTOM meeting ?
- FTIR / surface:
        Omaira & Dan: same stations as Ivan (exc. Ny-Alesund)
- FTIR / Umkehr: myself
- other techniques in HEGIFTOM (aircraft / UV-Vis / Lidar): volunteers ?
  HEGIFTOM 2022: External consistency
Izaña
See Ivan for detailed results
- Any other plans for tropospheric O3 satellite validation ?
  Satellite validation:
- FTIR / IASI-LISA tropospheric product (KOPRAFIT retrieval; G. Dufour & M. Eremenko): Yana
1. Development of strategy for comparison for St. Petersburg site (2021).
2. Testing the strategy at Kiruna and Izaña sites (2021-2022)
3. Expanding the comparison for other IRWG sites.

## Slide 8: OPT: Ozone and Precursors in the Tropics
Main goal: Assess the impact of tropical tropospheric ozone & precursors changes on global tropospheric ozone burden & radiative forcing
OPT data sets: O3, HCHO, CO, NO2
    In situ (sondes, surfaces, aircraft,…) long-term & campaigns
    Remote-sensing (satellite: OMI, IASI, TROPOMI, MOPITT,…. + ground-based: FTIR, UV-Vis, Aeronet)
    Models (WRF-Chem, GEOS-Chem,…)
Plans for publication:
    Present-day tropical ozone and precursors distributions → all tropical FTIR sites
    Tropical ozone and precursors trends → only long time-series (Mauna Loa; Altzomoni & Maïdo if long enough? ; Izaña 28°N if sub-tropics?)
    Impact of tropical ozone and precursors changes on global ozone
Leads: A. Gaudel & B. Sauvage
    FTIR contribution:
        I’ll provide O3 and HCHO; PIs will be co-authors if data used, as in TOAR-I
    I also promised CO: I can do it but if any volunteer is interested in joining with CO, I can share my work (as for O3: internal consistency ; quality check / interaction with PIs ; 0-8km column with uncertainties)
    Tropospheric NO2: Jim/Ivan ?

## Slide 9: TOP: Tropospheric Ozone Precursors
Main goals:
  Examine the global distributions and trends of key O3 precursors, and their uncertainties.
  Investigate factors that control the trends of ozone as a function of its precursors.
Leads: Y. Elshorbany & R. Seguel
Plans for publications:
  A review paper of global ozone precursor’s trends and variability in relation to ozone trends
  Call for other papers…
But: plans not so clear compared to the other WGs: no clear observation data sets (sometimes mention N2O and CH4 as well as O3, HCHO, CO, NO2 sometimes not); no clear models either….
FTIR contribution:
  I mentioned to Yasin that I can provide him O3, HCHO, and CO & I will do trend analysis (IGAC 2021)
  Any volunteer for CO, N2O, CH4 ?
There is less/no guarantee that FTIR data will be used; so I advise that volunteers invest time in data collection/ trends,… for their own interest first (as I do for O3, HCHO and CO)

## Slide 10: Summary
ALREADY PLANNED
HEGIFTOM:
  I’ll continue O3 internal consistency: interactions with you if errors not coherent in NDACC
  External consistency:
    Surface (Omaira, Dan)
    Sondes (Ivan, Isao)
    Umkehr (myself)
    Satellite (Yana; IASI/LISA)
  I’m planning O3 tropospheric trends study (IGAC 2021)
TOP and OPT:
  I’ll provide O3, HCHO, and possibly CO data: each PI will be associated to publications
  I’m planning HCHO, CO trend studies (IGAC 2021)
  Michel with Altzomoni data (plans?)
QUESTIONS/CALL FOR CONTRIBUTIONS
Any independent study on O3 and/or precursors that can be submitted in the TOAR-II special issue if relevant.
Any interest to join other WGs (East Asia, Urban,…) ?
HEGIFTOM:
  Testing / updating new strategy from Omaira ?
  Traceability ? Status / how to improve ?
  External consistency:
    Any other plans ?
TOP and OPT:
  Anyone wants to be in charge of CO ? Check internal consistency / data quality / interacting with PIs if necessary / 0-8km columns with uncertainties)
  Possible interest in TOP for N2O and CH4, but not so clear. Any volunteer to take care of this ?
  NO2 at polluted sites ?

## Slide 11: Extra-slides

## Slide 12
Comparison of tropospheric, upper troposphere/lower stratosphere, and stratospheric ozone columns using FTIR & sonde profiles
Ivan Ortega, James Hannigan, Omaira Garcia, Corinne Vigouroux, Dan Smale

## Slide 13
Data:
FTIR data: O3 files (HDF format) under the NDACC archive
O3 sondes: O3 sonde files (AMES format) under the NDACC archive
Initial Goal: This analysis started because there were some discussions about the phase of the FTIR free tropospheric annual cycle and in particular that it seems to peak early.
January 6th 2010.
For every sonde profile the O3 partial column in molec/cm2 and in Dobson Units are also calculated for each final grid altitude. Smoothing is not applied for the comparison with FTIR, but levels where partial columns are calculated should be similar.
Sites:
Eureka, Boulder, Izaña, Mauna Loa,
Lauder, Ny_Alesund
Notes: Ozone mixing ratios, in ppm, are calculated using partial pressures, then the raw O3 sonde data is re-gridded to a common grid (0.1 km) between 0.05 to 31.0 km using mean mixing ratios between these levels. The final grid altitude is 0.1, 0.2, 0.3, ... 30.9 km

## Slide 14
Izaña
Example: below is the comparison of tropospheric ozone at Izaña using all coincident observations (+/- 3h) – left and using seasonal cycle (15-days mean) – right.

## Slide 15
MLO (2012 - 2020) |  |  |  |  |  | 
 | Coincident (N=198) |  |  | Seasonal cycle (two weeks) |  | 
Column (km) | Median Bias (%) | σ (%) | r-value | Median Bias (%) | σ (%) | r-value
3.4 - 7.15 | 0.7 | 12.3 | 0.87 | 0.2 | 5.2 | 0.97
7.99 - 17.12 | 1.8 | 12.3 | 0.95 | 0.3 | 5.2 | 0.99
18.3 - 29.14 | 5.2 | 5.9 | 0.75 | 5.6 | 1.9 | 0.93
3.4 - 29.14 | 5.2 | 5.1 | 0.88 | 5.6 | 1.9 | 0.98
Boulder (2010 - 2020) |  |  |  |  |  | 
 | Coincident (N=134) |  |  | Seasonal cycle (two weeks) |  | 
Column (km) | Median Bias (%) | σ (%) | r-value | Median Bias (%) | σ (%) | r-value
1.6 - 8.87 | 2.8 | 10.3 | 0.8 | 3.0 | 6.2 | 0.86
9.7 - 18.31 | 5.4 | 9.7 | 0.98 | 4.9 | 5.5 | 0.99
18.31 - 26.2 | 7.6 | 6.7 | 0.84 | 8.3 | 3.0 | 0.95
1.6 - 26.2 | 6.4 | 5.3 | 0.95 | 7.6 | 2.3 | 0.99
Izaña (1999 - 2020) |  |  |  |  |  | 
 | Coincident (N=326) |  |  | Seasonal cycle (two weeks) |  | 
Column (km) | Median Bias (%) | σ (%) | r-value | Median Bias (%) | σ (%) | r-value
2.37 - 8.01 | 0.5 | 9.2 | 0.91 | 0.74 | 3.7 | 0.98
7.18- 18.31 | -0.6 | 10.0 | 0.96 | -1.9 | 4.1 | 0.98
19.54 - 29.14 | 3.5 | 5.1 | 0.74 | 3.8 | 2.0 | 0.92
2.37 - 29.14 | 2.3 | 3.9 | 0.93 | 2.8 | 0.9 | 0.99
Lauder (2001 - 2020) |  |  |  |  |  | 
 | Coincident (N=227) |  |  | Seasonal cycle (two weeks) |  | 
Column (km) | Median Bias (%) | σ (%) | r-value | Median Bias (%) | σ (%) | r-value
0.37 - 8.01 | 2.8 | 11.7 | 0.73 | 0.5 | 4.2 | 0.94
9.78 - 18.31 | 3.2 | 12.5 | 0.84 | -2.6 | 4.9 | 0.99
18.31 - 29.14 | 8.8 | 9.6 | 0.73 | 6.8 | 2.9 | 0.95
0.37 - 29.14 | 8.3 | 11.2 | 0.8 | 3.0 | 3.4 | 0.97
Summary

## Slide 16
Ny Alesund (1992 - 2020) |  |  |  |  |  | 
 | Coincident (N=67) |  |  | Seasonal cycle (two weeks) |  | 
Column (km) | Median Bias (%) | σ (%) | r-value | Median Bias (%) | σ (%) | r-value
0.024 - 8.01 | 6.5 | 11.5 | 0.79 | 5.9 | 3.9 | 0.97
8.01 - 17.12 | 1.7 | 7.5 | 0.98 | 1.2 | 5.0 | 0.99
18.31 - 29.14 | -0.2 | 9.3 | 0.85 | -0.9 | 3.3 | 0.95
0.024 - 29.14 | 1.42 | 7.3 | 0.94 | 0.9 | 2.5 | 0.99
Eureka (2006 - 2019) |  |  |  |  |  | 
 | Coincident (N=67) |  |  | Seasonal cycle (two weeks) |  | 
Column (km) | Median Bias (%) | σ (%) | r-value | Median Bias (%) | σ (%) | r-value
0.61 - 8.02 | 7.1 | 10.0 | 0.82 | 7.9 | 4.0 | 0.96
7.2 - 17.12 | 4.3 | 9.6 | 0.95 | 4.64 | 5.9 | 0.99
17.12 - 27.66 | 4.3 | 8.9 | 0.86 | 3.6 | 5.7 | 0.92
0.61 - 27.66 | 6.1 | 9.5 | 0.89 | 6.2 | 5.2 | 0.96
Summary

## Slide 17
Remarks
Biases < 5% are typical in the low & free troposphere and stratosphere.
Some factors may affect the comparison, e.g., sampling of air masses. Ideally, we should characterize the horizontal differences using LOS and location of sonde.
No clear evidence of out of phase FTIR ozone columns in the troposphere.
This kind of comparison my be used to compare/characterize new products in the near-future, e.g., using new spectroscopy.

## Slide 18
  Traceability
Some parameters are available in the geoms HDF files archived in NDACC (a priori ozone profiles, p, T)
A metadata file is also available at each site with information such as the instrument / instrument change; the retrieval code; some publications with information on retrievals,…
Some guidelines for retrievals in the IRWG website: https://www.acom.ucar.edu/irwg/IRWG_Uniform_RP_Summary-3.pdf
In summary:
  Site dependent.
  Automatization chain with full traceability is in progress within the project ACTRIS.

## Slide 19
FTIR for TOAR-II: Ozone data
→ 15 to 16 FTIR stations with ≥ 10 years of data in TOAR-II, to be used for trend analysis.
7 stations with sparse or short time-series, can be used for validation (satellite / ground-based)

## Slide 20
→ 15 to 16 FTIR stations with ≥ 10 years of data in TOAR-II, to be used for trend analysis.
7 stations with sparse or short time-series, can be used for validation (satellite / ground-based)
Stations / Covered period | 95 |  |  |  |  | 00 |  |  |  |  | 05 |  |  |  |  | 10 |  |  |  |  | 15 |  |  |  |  | 20
Eureka 80°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Ny-Alesund 79°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Thule 77°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Kiruna 68°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Harestua 60° |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
St-Petersburg 60ºN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Bremen 53N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Zugspitze 47ºN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Jungfraujoch 47°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Toronto 44ºN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Rikubetsu 43°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Boulder 40°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Tsukuba 36°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Izaña 28°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mauna-Loa 20°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Altzomoni 19°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Paramaribo 6°N |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Porto Velho 9°S |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Reunion Island StDenis 21°S |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Reunion Island Maido 21°S |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Wollongong 34°S |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Lauder 45°S |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Arrival Heights 78°S |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 stations were used in TOAR
7 to 8 stations with ≥ 10 years of data added in TOAR-II

## Slide 21: OPT Data sets
Observations of O3 and precursors (CO, NO2, HCHO)
Models
In situ
IAGOS (aircraft)
SHADOZ (sondes)
Surface measurements: TOAR database, Delhi region, ATTO tower in Amazonia, Kenya surface ozone, site in Peru
Campaigns observations
Remote sensing
Regional
WRF-Chem
Global
ECHAM6-HAMMOZ
DOSE
FRSGC/UCI
GEOS CCM
GEOS-Chem
ATom
HIPPO
AMMA
STARE
LBA
TROPOZ I & II
TRACE A
DECAFE
SAFARI
EXPRESSO
PEM TROPICS
TROCCINOX
DACCIWA
SEAFIRE
OMI
IASI
TES
TROPOMI
MOPITT
OMPS
EPIC
TOMS
FTIR network
MAX DOAS
AOD – Aeronet