## Slide 1
Quantifying the impact of the COVID-19 pandemic restrictions on CO, CO2, and CH4 in downtown Toronto using open-path Fourier transform spectroscopy
Yuan You1, Brendan Byrne2, Orfeo Colebatch1, Richard L. Mittermeier3, Felix Vogel4, and Kimberly Strong1
1Department of Physics, University of Toronto;
2Jet Propulsion Laboratory, California Institute of Technology;
3Air Quality Research Division, Environment and Climate Change Canada;
4Climate Research Division, Environment and Climate Change Canada
2021 online IRWG Meeting C
June 4, 2021

## Slide 2: Outline
Overview of the project and measurement setup
Results during the COVID-19 pandemic restrictions
Summary
Results in this presentation are under review for Atmosphere.

## Slide 3: Open-Path FTIR in Toronto
Bruker 125M FTIR spectrometer with telescope and retroreflector
CO2, CO, CH4 ,N2O, H2O, and HDO are quantified since November 2017
Two co-located weather stations
Measurements are made continuously day and night
Retrievals use the Multiple Atmospheric Layer Transmission (MALT) code version 5 (Griffith, 1996).
Results of measurements from November 2017 to December 2018 are published in Byrne et al. (2020)
Figures are adapted from Brendan Byrne et al., Monitoring urban greenhouse gases using open-path Fourier transform spectroscopy, Atmosphere-Ocean, 58(1), 25-45, 2020.
N

## Slide 4: Motivation
Drop in daily traffic counts: 50% and 30% during 2020 and 2021 stay-at-home periods, respectively.
72% of CO emissions of Ontario are from transportation and mobile equipment. (APEI, 2018).
35% of Toronto’s GHG emissions in 2018 were from on-road vehicles. (City of Toronto, 2018)
The goal of this study: (1) quantify the changes in mole fractions and enhancements of CO, CO2, and CH4 in downtown Toronto during the COVID-19 stay-at-home periods in 2020 and 2021; (2) to determine whether this system could detect the impact of changes in urban traffic emissions on CO and CO2.
Year | Period 1 | Period 2
2018 | 13 January to 13 March | 14 March to 18 May
2019 | 13 January to 13 March | 14 March to 18 May
2020 | 13 January to 13 March | 14 March to 18 May
 | Period 3 | 
2021 | 14 January to 7 March | 
[Normalized daily traffic counts are from Apple mobility data (http://covid19.apple.com/mobility) for the Greater Toronto Area.]

## Slide 5: Method
Mole fractions are retrieved using MALT 5 algorithm
To investigate the impact on mole fractions due to local emission sources, the mole fraction enhancement above background (Δ gas) is calculated for CO, CO2 and CH4
Δgas = mole faction (gas) – background (gas)
background (gas) = 5th percentile of mole fraction (gas) in 5-day running window
Daily mole fractions and enhancements above background in the afternoon (from 12:00 to 16:00 local time) were extracted and averaged into daily results.
[Ammoura et al. (2016); Super et al. (2017); Communication with Felix Vogel]

## Slide 6: Results - Daily statistics during 12:00-16:00 local time
Mole fraction
Mole fraction enhancement from background
The mean afternoon CO (ΔCO) for 2020 P2 shows a decline of 19±6% (51±23%) relative to 2020 P1. For ΔCO, differences between P1 and P2 in 2018 and 2019 are not significant.
CO (ΔCO) for 2021 P3 also shows a decline of 12±7% (42±24%) relative to 2020 P1.
Only in 2020 is the difference of mean afternoon ΔCO2 between P1 and P2 significant. The mean afternoon ΔCO2 declined by 3.9±2.6 ppm (36±24%) during 2020 P2 compared to 2020 P1.
The mean afternoon CH4 during 2020 P2 and 2021 P3 declined by only 1.6±1.2% and 1.7±1.2% respectively relative to 2020 P1. ΔCH4 did not show significant decline during 2020 P2 relative to 2020 P1. The variability in CH4 and ΔCH4 between periods and years is likely influenced by local sources.
stay-at-home
stay-at-home

## Slide 7
Results- Diurnal variations of ΔCO on weekdays
Δ CO_peak = Δ CO_high – ΔCO_low
Δ CO_high = average from 8 to 9 AM
Δ CO_low = average from 3 to 6 AM
Except for 2020 Period 2
Δ CO_high = average from 7 to 8 AM
Δ CO_low = average from 3 to 6 AM
 | 2018 | 2019 | 2020 | 2021
Δ CO_peak P1 – P2 (ppb) | 7.5 | 25.3 | 23.3 (53%) | 10.9
t-test p value | 0.53 | 0.18 | 0.013 | 0.28
95% confidence | not | not | significant | not
Only in 2020 is the change in the ΔCO peak amplitude between P1 and P2 significant. This is consistent with the reduction in local traffic during the 2020 P2.
Median
Mean

## Slide 8: Results- Changes in local traffic and Δgas
y = 0.176x – 4.11, r2 = 0.91
y = 0.739x – 22.2, r2 = 0.85
Local traffic data: the Don Valley Parkway or Gardiner Expressway with Gerrard Street, Bay Street, or Windermere Avenue.
Daily afternoon traffic counts are normalized and traffic data from the three traffic sites are averaged. Daily results of Δgas vs normalized average traffic are grouped before the linear regression analysis.
Linear relationships of the average results of ΔCO and ΔCO2 with traffic are observed with slopes of 0.74 ± 0.15 ppb and 0.18 ± 0.05 ppm per percentage change in traffic, respectively.

## Slide 9: Summary
The OP-FTIR system in this study detected changes in surface mole fractions and enhancements above background of CO and CO2 in downtown Toronto during the COVID-19 stay-at-home periods.
The mean afternoon ΔCO declined by 23 ± 10 ppb (51 ± 23%) and 19 ± 11 ppb (42 ± 24%) during the stay-at-home periods in 2020 and 2021 respectively compared to that for 2020 reference period. For ΔCO2 the declines are 3.9 ±2.6 ppm (36 ± 24%) and 3.5 ± 2.8 ppm (33 ± 26%) in 2020 and 2021, respectively.
The mean amplitude of ΔCO diurnal variation declined by 53 ± 42% during the stay-at-home period in 2020, compared to the 2020 reference period.
The OP-FTIR system should be able to detect traffic emission changes after a significant portion of the transportation sector has transitioned to electric vehicles as planned for Toronto in the coming years.