## Slide 1: Linelist migration
Motivation
Current status
Proposed way forward
Jim Hannigan & Manu Mahieu

## Slide 2: Linelist migration: motivation
Current linelists are HITRAN08 or HITRAN00
New releases of HITRAN and Geoff’s ATM linelists potentially include improved line parameters that may:
  Reduce fitting residuals
  Improve the SYS & RAN uncertainty budgets: better handling of interferences (H2O), more precise line parameters (e.g., HITRAN quoted errors)
  Minimize oscillations in the retrieved profiles: allowing freeing regularizations, to the benefit of DOFS
Most communities have updated their linelists (e.g., for satellite retrievals) => this could be problematic for satellite validation exercises using our standard products (systematic biases…)
The new/latest SFIT-4/PROFFIT, WACCM_1980-2040, hdf template and NDACC-DHF host all coincide and adopting more current and better line parameters at the same time makes sense
Still, a new linelist could in some instances potentially worsen the fits! => careful check of the new candidate parameters is needed, using sites with dissimilar atmospheric conditions (altitude, humidity, pollution…)

## Slide 3: Linelist migration: current status
We are not starting from scratch
In 2019, tests were conducted by many of us, involving eight different sites, HITRAN16 and ATM18, the 10 official species as well as OCS and H2CO (for which HITRAN2008 is not used)
In brief, the conclusions from the Wanaka meeting were:
  No improvement or even degradation for CH4
  Improvement for CO, O3, ClONO2
  Essentially a status quo was reported for the other gases
in some instances, these tests called for strategy updates: N2O (add HDO in 3µw) and HCN (strategy needs improvement/adjustment for wet sites)
Since then improvements to ATM including water vapor.
Notes: Note however that CH4 in ATM16=HIT08

## Slide 4: Linelist migration: proposed way forward
For SFIT-4 users, switch to the new official version (compatible with the latest HITRAN releases; e.g., isotopologues)
HITRAN16 remains current (there are updates on hitran.org, how do we make sure to accommodate for them?)
Test ATM20 (from Geoff, release date?) for all species
Report results in a homogenized manner:
  Testing for every sites, every species, HIT16 and ATM20, for 2 years
  Description of the adopted regularizations
  Provide tables (excel, ascii) for HIT08, HIT16 and ATM20 including:
    Date, spectrum SNR, SZA, TOTCOL, FITRMS, DOFS, RND(%), SYS(%)
  Provide graphs of retrieved profiles for the 3 linelists; correlations with prominent interfering species (e.g., H2O), plots of TOTCOL differences with HIT08, as a function of time
  Your conclusions
Notes: The HITRAN2020 – ASA meeting in Reims has been postponed to Aug. 2021.

## Slide 5: Linelist migration: proposed way forward
Target | Site A / Team A | Site B / Team B | Note
CO |  |  | 
C2H6 |  |  | 
CH4 |  |  | 
N2O |  |  | 
HCN |  |  | 
HNO3 |  |  | 
ClONO2 |  |  | 
HCl |  |  | 
HF |  |  | 
N2O |  |  | 
O3 |  |  | 
Suggested allocated time: finish testing before end of September
Discussion and evaluation at a dedicated online meeting in October?
Notes: Note that we should allow for enough time. Several teams will have to implement the new SFIT-4 and related environments before they can start.