## Slide 1
Alignment tool kit
120HR Laser holder
Microscope and Telescope
Plus height spacer
Holder for diffuser paper
Internal laser beam blocker
We assembled a kit of simple, low cost 3D-printed tools for checking alignment of the Bruker FTS. The parts can be left on-site at remote laboratories, or are small enough to travel as carry-on luggage. Standard off-the-shelf optics are used.
The microscope and telescope are identical, so only one is needed, although it is practical to make one of each and optimise the optics for each application (e.g. used preferred eyepiece).
Contact: john.robinson@niwa.co.nz
Alignment docs: https://tccon-wiki.caltech.edu/Main/AlignmentOfThe125HR (under construction)
125HR Laser holder

## Slide 2
The telescope shelf hangs at the correct height support the telescope to view apertures in the 120 and 125. It folds down flat for travel. The telescope can also be used as a microscope, with a spacer, to view fringes from within the interferometer compartment.
Telescope shelf
Shelf with Telescope
Microscope in interferometer
Alignment toolkit