## Slide 1
CO2, CH4 and CO at Xianghe

## Slide 2
Xianghe site
The Xianghe site (39.75° N, 116.96° E) lies in a suburban area,
~ 50 km southeast of Beijing.
2nd TCCON site in China

## Slide 3
Xianghe observations
Picarro CRDS analyzer G2301
Insitu CO2 and CH4
60 m above surface
Bruker IFS 125 HR spectrometer
XCO2, XCH4, XCO
Since June 2018
Observations carried out in collaboration with the Institute
of Atmospheric Physics of the Chinese Academy of Sciences (IAP-CAS)
1 year

## Slide 4
Xianghe observations
Observed timeseries of CO, CO2 and CH4 show lots of variability

## Slide 5
How accurate is WRF-GHG in simulating the different observations types of CO2, CH4 and CO at Xianghe? What are the model’s strengths and weaknesses?
What are the driving factors behind the observed variabilities?
  What are the different (sector) contributions to the observed concentrations (surface and column)?
Research questions
Previous case study: TCCON, NDACC and ICOS data at Réunion Island
(Callewaert et al, 2022, ACP)

## Slide 6
WRF-GHG model
Regional atmospheric transport model
Simulation of 3D meteorological and chemical fields over time
WRF-GHG is WRF-Chem in the passive tracer option: no chemical interactions
Outside domain d01:
Boundary conditions = background
ERA5 and CAMS reanalysis
Inside domain d01:
Surface – atmosphere fluxes (uptake and emissions) from different sources
CAMS-GLOB-ANT
REAS
FINN
WetCHARTs
…

## Slide 7
Passive tracers
The simulated concentration of a gas is split up into the contributions of different sources. For example CO2:
Anthropogenic emissions
Biomass burning emissions
Ocean uptake
Biosphere fluxes
Initial and boundary conditions
Flux field
Concentration field
Anthropogenic tracer
Biomass burning tracer
Ocean tracer
Biosphere tracer
Background tracer
sum
Total simulated CO2
Concentration field

## Slide 8
WRF-GHG model setup
Split anthropogenic tracer into different source sectors
CAMS-GLOB-ANT provides information about 11 sectors
 Aggregate into 5 sectors
CAMS-GLOB-ANT sectors | WRF-GHG flux fields
Residential, commercial and other combustion | Residential & Waste
Solid waste and waste water treatment | 
Industrial processes | Industry
Power generation | Energy
Fugitive emissions from solid fuels | 
Oil refineries and transformation industry | 
Agriculture livestock | Agriculture
Agriculture soils | 
Agricultural waste burning | 
Non-road transportation | Transportation
Road transport | 

## Slide 9
Results
Model – data comparison

## Slide 10
WRF-GHG 1 year simulation
1 September 2018 – 1 September 2019
Comparing hourly model output with observations:
In situ | FTIR
Horizontal grid cell of instrument | Horizontal grid cell of instrument
Model profile interpolated to 60m above model surface | Model profile extended (above 50 hPa) with TCCON a priori + smoothed
Mean of all observations within 15 min of model hour | Mean of up to 5 observations within 20 min of model time

## Slide 11
WRF-GHG accuracy?
 | XCO2 | XCH4 | XCO
BIAS | -1.41 ppm | -3.31 ppb | 0.35 ppb
RMSE | 2.40 ppm | 23.36 ppb | 31.07 ppb
 | In situ CO2 | In situ CH4 | 
BIAS | 2.52 ppm | 9.43 ppb | 
RMSE | 20.94 ppm | 251.82 ppb | 
CORR: 0.85
CORR: 0.56
CORR: 0.69
CORR: 0.68
CORR: 0.56

## Slide 12
What is driving variability?
XCO2 – October 2018
XCH4 – October 2018
XCO – October 2018
All columns increase on same days
These polluted days can be linked with simulated wind direction
XCO2
XCO
XCH4
SW: high
(North China Plain pollution)
NW: low

## Slide 13
What is driving variability?
Polluted days also visible in timeseries of insitu data
Strong correlation between the daytime mean insitu and column concentrations.
Impact of polluted / clean airmasses is important for both columns and observations near the surface.

## Slide 14
What is driving variability?
For surface observations, daily variation in planetary boundary layer height is also important.
Concentrations peak around 7-8h local time.
Minimum values are found around 15h.
This can be linked to the variation in the PBLH:
Accumulation near the surface at night
Dispersion in the mixing layer during the day

## Slide 15
Sector contributions?
Tracer contributions above background for CO2
Main sectors:
Industry – Energy – Residential – Transportation - Biogenic
Ocean and biomass burning less relevant at Xianghe
Biosphere is a CO2 source from October until April
Residential emissions are larger in Winter
Column
Insitu

## Slide 16
Sector contributions?
Tracer contributions above background for CH4
Main sectors:
Energy – Residential & Waste – Agriculture
Industry, transportation, wetlands, termites and biomass burning less relevant at Xianghe
Residential emissions are larger in Winter
Column
Insitu

## Slide 17
Sector contributions?
Tracer contributions above background for CO
Main sectors:
Industry – Residential – Transportation
Column
Energy and biomass burning less relevant at Xianghe
Residential contributions are larger in Winter

## Slide 18
Main conclusions
Polluted/clean airmasses
Variability in timeseries
Column data
depending on wind direction
Insitu data
polluted/clean airmasses depending on wind direction
PBL height
Local hotspots + wind direction
WRF-GHG strengths
Accurate simulated timeseries
Accurate diurnal cycles
Ability to split signal into several tracers
Link between tracer concentrations and meteorology
WRF-GHG weaknesses
Dependence on boundary conditions
Dependence of accurate flux information

## Slide 19
sieglinde.callewaert@aeronomie.be
thank you! questions?