## Slide 1
Designing additional GHGs observations network over Korea using Lagrangian inversion model
Samuel Takele Kenea1, Sangwon Joo1, Shanlan Li1,, Sumin Kim1, Young-SuK Oh1, Daegeun Shin1, Soojeong Lee1, Lev, D. Labzovskii2, Sanghun Park3
Climate Research Department, National Institute of Meteorological Sciences (NIMS), 33, Seohobuk-ro, Seogwipo-si 63568, Jeju-do, Korea
R&D Satellite and Observations Group, Royal Netherlands Meteorological Institute (KNMI), 3731GA De Bilt, The Netherlands
Laboratory for Atmospheric Modeling Research, Yonsei University, Seoul, Korea
Contact: samueltakele81@gmail.com
NDACC-IRWG-TCCON-COCCON meeting 2023

## Slide 2
Uncertainty in anthropogenic emissions is a fundamental science question
The aim of this work is to propose new additional GHGs (CO2) candidate sites, which will enable us to improve GHGs emissions at fine spatiotemporal scales over Korea.
We need to have
simulated footprints (e.g., KIM-STILT model), together with Bayesian inverse modelling framework
Meteorological deriving fields are obtained from KIM (Korean Integrated Model)
prior and true GHGs emissions data at high spatiotemporal resolution,
defined model-data mismatch errors, priori flux uncertainties, and error correlations
Introduction

## Slide 3
Aircraft
(Nara)
Vessel
(Gisang)
Anmyeon-do
(AMY)
Ulleung-do
(ULD)
Jeju Gosan
(JGS)
Boseong
(BST)
Lotte
(LTT)
Ground FTS
In-situ surface
GHG monitoring network in Korea
Measurement activities operated by NIMS
Platform description
  In situ surface (AMY, JGS, ULD)
  Tall tower (LWT, BST)
  Mobile (Vessel, Aircraft)
  Remote observation (FTS, mobile FTS)
  Low cost sensors are under developing stage
Measurement details
  CO2/CH4/N2O/SF6
Data Visualization
  Observation data
  Model data

## Slide 4
Korea CO2 emission sectors based on EDGAR data
Major contributions
Main Activity Electricity and Heat Production 48.2%
Road Transportation no resuspension 14%
Manufacturing Industries and Construction 11%
Other sectors 8.5%

## Slide 5
Table 1. List of GHG observation sites including existing and new candidate sites over Korea.
STILT (Stochastic Time Inverted Lagrangian Transport, Lin et al. 2003)
  horizontal resolution - 0.1˚ x 0.1˚ lat-lon
  Temporal resolution - 1-hour
  Number of particle - 500
  Backward time – 3 days
The footprint – quantifies the influence of upwind surface fluxes on the concentrations measured at the receptor and is computed by counting the number of particles in surface-influenced volume and the time spent in that volume.
KIM (Korean Integrated Model, Hong et al., 2018 ) for meteorological data
  horizontal resolution- 0.125˚ x 0.125˚ lat-lon
  Temporal resolution - 3-hour
  Vertical levels - 31
Footprints
Figure 1. KIM-STILT aggregated footprints of 10 sites located in Korea, December 2020 (2-7 UTC).
No | Site | Lat. (˚N), lon. (˚E), | STILT height (m.a.g.l)
1 | Anmyeondo (AMY) | 36.538576, 126.330071 | 40
2 | Gosan (JGS) | 33.29382, 126.16283 | 12
3 | Ulleungdo (ULD) | 37.48, 130.90 | 10
4 | Lotte World Tower (LWT) | 37.5126, 127.1025 | 550
5 | Boseong Tower (BST) | 34.76, 127.21 | 140
6 | Ulsan (ULS) | 35.52636, 129.293686 | 20
7 | Busan (BSN) | 35.1573, 129.1797 | 40
8 | Jeonju (JOJ) | 35.8026, 127.1182 | 40
9 | Daejeon (DJN) | 36.3359, 127.4576 | 40
10 | Jinju (JNJ) | 35.16425, 128.10732 | 40

## Slide 6
Bayesian Inverse Method
Posterior emission estimates are optimized through the minimization of the cost function
(1)
(2)
,
R- covariance of model-mismatch error, Q-covariance of prior emissions,-error
The posterior best estimate of emissions, , is expressed as:
(3)
Posterior uncertainty covari­ance matrix , is given as:
(4)

## Slide 7
CO2 emissions
EDGAR v6
  horizontal resolution - 0.1˚ x 0.1˚ lat-lon
  Temporal resolution - monthly
  the latest available data is December 2018
  Constructed as a prior emission
  Diurnal scaling factor (from Nassar Emissions Scale Factors) is applied
GRACE2021 (Dou et al. 2023)
  horizontal resolution - 0.1˚ x 0.1˚ lat-lon
  Temporal resolution - daily
  near-real-time daily national CO2 emissions estimates (Carbon monitor), multi-source spatial activity data emissions
  Satellite NO2 data for time variations
  Diurnal scaling factor (from Nassar Emissions Scale Factors) is applied
  Constructed as a true emission
Figure 2. CO2 emissions for December 2020.
Unit for emission is µmol m-2 s-1.

## Slide 8
Model-data mismatch (R)
R typically reflect inaccuracies in the transport, prior fluxes, and measurements
Vertical mixing layer height error is approximated of 7% mean enhancement adopted from Gerbig et al. (2008),
representing error for afternoon time period only.
Horizontal wind error is assumed to be 35% of mean enhancement (Kunik et al., 2019), with a correlation time
scale of 2.8 hours (Mallia et al., 2017)
uncertainty in STILT based on the finite number of particles released is considered 0.1 ppm (Mallia et al., 2017;
Kunik et al.,2019)
Error introduced by aggregating spatially and temporally heterogeneous fluxes into one homogeneous grid cell
and timesteps (followed Kunik et al. (2019) approach)
Prior error covariance (Q) describes both variance in prior emissions uncertainty and spatial and temporal correlation of these uncertainties.
Error covariance parameters
Exponential decay equations
)
)
horizontal length scale = 45 km, temporal length scale = 5 days

## Slide 9
Uncertainty reduction
Daytime (2-7 UTC) uncertainty reduction =
19.1 % (5 sites) 29.7 % (10 sites)
Figure 3. Prior uncertainty and uncertainty reduction maps. Unit for emission is µmol m-2 s-1.
Reduced χ2 = 0.926
Prior uncertainty from absolute difference of prior minus true emission
The assigned model-mismatch values are ranging between 2.44 ppm and 3.28 ppm
ULD site only does not have influence on the uncertainty reduction
Uncertainty reduction

## Slide 10
Influence of spatial and temporal correlation length
Ranking the site influence in terms of uncertainty reduction
Investigate the impact of inlet heights, backward time of the trajectory
Undergoing work: sensitivity analysis and method validation

## Slide 11
Thank you!