## Slide 1
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
Anmyeondo station report and Long-term variability characteristics of FTS spectra.
Young-Suk Oh*, Su Ryon Shin, Nicole Bassous, Hyun Young Jung, Chang Kee Lee, Sangwon Joo, Myoung-Hwan Ahn, Mina Kang , Sang-Woo Kim, Jeongsoon Lee, ,Sumin Kim, Soo Jeong Lee, Shanlan Li, Samuel Takele Kenea, Nicholas Deutscher, David Griffith.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
I would like to shear the information of AMY station with you through the presentation, The key is site reports and ongoing research

## Slide 2
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
Contents
1. Anmyeondo Station Report
2. Observational data from AMY.
3. AMY data processing. (GGG2020)
4. Long-term variability characteristics of FTS
5. Non-contact, Low-cost GHG Sensor (Graphene-Based)
6. EM27/SUN equipment validation and operation.
7. Conclusion

## Slide 3
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
1. Anmyeondo Station Report
※ AMY’s History
* Installed IFS 125HR equipment in 2013.
* Designated AMY-TCCON station for 2014.
* 2018 GPS replacement and alignment calibration performed.
* Solar tracker and laser replacement in 2019.
* GGG2020 installation operation in 2021.
* Laser and Cam replacement in 2022.
* 2023 EM27/SUN operation and IFS125HR alignment calibration performed.
AMY : Co-located with GAW site in-situ measurements, Capture east Asia outflow, Model and Satellite validation and for carbon cycle science.
The flow of this figure is the AMY history. We have been running station for 10 years. After designation, there was an issue

## Slide 4
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
※ AMY’s Equipment
1. Anmyeondo Station Report
OPD (cm)
OPD (cm)
Before Alignment.
After Alignment.
* The ME as a function of OPD is picture, but reaches 1.033 at 45cm OPD. While the alignment is still within the broad TCCON criterion of ME being within 5% of ideal, is had clearly degraded in the 3.5years since the previous analysis.
* The resulting ME as a function of OPD is shown. The ME and 45cm OPD is now 1.008, well within the ideal TCCON range.
AMY station equipment meets TCCON standards,. The data will go through QA/QC and be provided soon.

## Slide 5
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
2. Observational data from AMY.
[GGG 2014(2014.4~2022.5)]
(2019.4)
(2019.12)
(2020.6)
(2020.11)
Period of unavailability of data.
(Solar tracker and laser replacement)
Period of without data.
(OPUS and Mirror replacement)
√. AMY data has been produced from March 2014 to the present of 2023. (However, GGG analysis was completed by May 2022.)
√. The average increase in GHG concentration for 8 years of AMY is 3.1ppm/year (XCO2), 9ppb/year (XCH4), and 1.9ppb/year (XCO).
( AMY data is of sufficient quality to detect the amount of variation.)

## Slide 6
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
3. AMY data processing. (GGG2020)
Config
Spectra
Tccon
Windows
Levels
Models
Vmrs
Mod_vmr_maker
Ncdf
Cell_status_info
Linelist
Isotopologes
Apriori
Src bin
Sunruns
Runlogs
Install
Spt
Ak
Tsen_cofts
History …
Observation
First-Guess
Other info
Outputs
Run shell
Path
Observation
First-Guess
Other info
Iterative process gfit
╊
Forward model
Output
(VFS for gases and others)
* VFS: Volume-mixing-ration Scaling Factor
Run shell
GGG2020
[GGG 2020(2021.1~2022.05)]
AMY’s data information.
( http: // 175 . 213. 240. 12 : 7855 )
It shows data processing using AMY Station’s GGG2020. We produced data using GGG2020 from January 2021.

## Slide 7
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
4. Long-term variability characteristics of FTS
※ Seasonal characteristics of AMY.
DJF (Winter(December – February))
MAM (Spring(March – May))
JJA (Summer(June – August))
SON (Autumn(September – November))
* The sensitivity of CO2 concentrations (ppmwith the calculated using the FLEXPART model with the AMY station in 2018.
* The footprints of Asian station mainly span countries bordering the East Sea, i.e. Korea, Japan, the Russian Far East and eastern China. Although the coverage of these station is relatively small, the main industrial centers in the region are included.

## Slide 8
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
4. Case Research: Altitude characteristics of AMY
CO2 vertical profile calculation according to wavelength/ channel of AMY.
Two windows with high vertical sensitivity and TCCON1, TCCON2 windows are used.
(TCCON 1: 6220cm-1, TCCON 2: 6339cm-1, Strong: 4852 cm-1, Weak: 6074cm-1)
Differences in the temperature profile of the low layer affect the CO2 altitude profile .
Therefore, window information that is sensitive to the low layer is required .
* NIMS plans to conduct a campaign to generate additional information. (July- September 2023.)
Participating equipment: FTS, M-FTS, Aircraft, Satellite, Radio zone, Tower, AERI, Lidar, Photometer, Low cost sensor, etc.

## Slide 9
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
√. Analysis of window characteristics sensitive to height by period and season in AMY. In the future, analysis will be conducted on the entire data from 2022 to 2023, and CH4 will also be added.
(2021.1.10.)
(2021.2.22.)
(2021.7.10.)
(2021.7.23.)
As the analysis data, the channel/ wavelength sensitive to the low layer was identified as a strong window(4852 cm-1).
4. Case Research: Altitude characteristics of AMY

## Slide 10
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
=Transmittance/XCO2
* The peak is distributed at an altitude of 3 to 10km in the form of complex Jacobion. (11 a.m., KST.)
Source tracking analysis using Footprint (STILT model): Altitude: 5km, Time: 11 am, KST)
Comparative analysis of footprint results and satellite information on April 4.
( affects the area near AMY)
4. Case Research: Source tracking characteristics of AMY

## Slide 11
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
5. Non-contact, Low-cost GHG Sensor (Graphene-Based)
(ref: Nano Letters, Young-Suk Oh at al. 2022.6.20.)
CO
CO2
CH4
N2O
H2O
HF
HDO
Sun Source
GHG
Distance
Photoelectric
Detector
The light energy absorbed by the GHGs
The photocurrent of the graphene detector
* GHG measurements of Graphene Photoelectric – Based Detector
* Detection Methods: The graphene photocurrent generated by the light passing through the GHG layer is reduced compared to the photocurrent generated by the light passing through the vacuum layer without the GHG.
* By measuring the amount of change in the reduced photocurrent, it becomes possible to detect GHGs.
Responsivity according to the concentration of GHG

## Slide 12
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
6. EM27/SUN equipment validation and operation.
* Preparing for EM27 operation and designation of COCCON stations.
We will prepare for EM27 operation and COCCON station designation.
Therefor, research is underway to verify the operated data.
* Designation of COCCON station in Korea
AMY station in GAW
Ewha University station in Seoul

## Slide 13
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023
7. Conclusion
1. The conclusion is as follows. Our AMY station is operating from 2014 to the present in 2023, and the observation data analyzes the characteristics of GHG fluctuations.
2. Our AMY station is producing data using both GGG2014 and GGG2020, and is researching climate change characteristics with the production data.
4. We are also conducting research in new fields. The studies are “Low-cost sensor” and “EM27/SUN”. A daemon version of that sensor was built. And EM27 has started operating and is pushing to join COCCON.
3. We are analyzing three characteristics of climate change. GHG sensitivity, concentration distribution by altitude, source tracking.
We always welcome your participation in research.

## Slide 14
Thank You.
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
We always welcome your participation in research.
Acknowledgment: This work was funded by the Korea Meteorological Administration Research and Development Program under grant KMA2018-00522 and KMI2022-01610
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
NDACC-IRWG-TCCON-COCCON Annual Meeting 2023

## Slide 15
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
Here are the footprint distributions for AMY site (Figure 1), which were considered a 5-day backward time to look at the source influence regions. Unit for footprint is given in log10 (ppm/µmol m-2 s-1).

## Slide 16
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
Figure 2. OCO-2 XCO2 (ppm) (left panel) and ∆XCO2 = XCO2-mean(XCO2) (right panel). The marked one by circle is a Taean power plant?
Figure 3. Footprint distribution at AMY. It is considered 12-hour backward time. Unit for footprint is given in log10 (ppm/µmol m-2 s-1).

## Slide 17
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
: total resistance, : electrical conductivity, L: graphene rod length
A: contact area, : contact resistance
Of some interest, this structure showed an interesting potential for infrared optical light absorption.
Electrical conductivity in the graphene sheet-stacked device increased as light intensity increased.
The photo-induced detection stability of our GHG photoelectric device was confirmed by generating a constant photocurrent at a constant applied voltage (5 V of for on) over several tens of cycles.

## Slide 18
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
(100
This characteristic of the GHGs provides clear evidence that a fraction of the incident light energy is absorbed in the from of heat energy by the GHG media.
The correlation between generating a photocurrent proportional to the number of photons when the light intensity incident on graphene surfaces, after passing through CO and CO2 media, at a given time, increases.
and are the electrical conductivity in ambient gas and the electrical conductivity under vacuum, respectively.

## Slide 19
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
Photoelectric conductivity of the graphene detector via light passing through a carbon dioxide medium in a vacuum and the atmosphere.
Since the change in the resistance of the element according to temperature is reflected in the electrical conductivity of a vacuum, the change in conductivity according to temperature is not considered in the responsivity calculation when detecting GHGs.
It should be emphasized that this GHG detection device is not affected by temperature.
The change in electrical conductivity with respect to mass flow is not considered because it is insignificant.

## Slide 20
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
CO2
CH4

## Slide 21
National Institute of Meteorological Sciences, Young-Suk Oh, ysoh306@korea.kr, ysoh306@korea.kr, 2023.06.13.
Residuals (Measured – Simulated)
CO2
CH4