## Slide 1
COCCON activities during the 2021 La Palma volcano eruption
N. Taquet, O. García, R. Campion, T. Boulesteix, W. Stremme,
C. Rivera, M. Grutter, A. Barreto, O. Álvarez, S. León-Luis, R. Ramos,
V. Carreño, F. Almansa, F. Hase, T. Blumenstock
noemie@atmosfera.unam.mx, ogarciar@aemet.es
NDACC-IRWG/TCCON/COCCON Annual Meeting, 13 June 2023

## Slide 2
- Eruption period: Sept. 19 - Dec. 13, 2021 (85 days)
- Most recent subaerial eruption in 50 yr
- Volcanic explosivity index (VEI) of 3
- Lava flows covered more than 1.200 ha (infrastructures, towns, crops,...)
La Palma Volcanic Eruption
La Palma
IZO
Volcano
Notes: The Volcanic Explosivity Index (VEI) is a scale that describes the size of explosive volcanic eruptions based on magnitude and intensity. The numerical scale (from 0 to 8) is a logarithmic scale, and is generally analogous to the Richter and other magnitude scales for the size of earthquakes.

## Slide 3
MOUNTS project
TROPOMI processing
Valade et al. (2019)
La Palma Volcanic Eruption
Phase I: alternating explosive and effusive activity, emissions at different vents.
Phase II: less energy in the volcanic system, intense effusive activity (more lava flows, less aerosol and gas emissions)
Total SO2 amount released: 1,84 Mt
Phase I
Phase II

## Slide 4
La Palma Volcanic Eruption
Transport to Europe, America and Africa in the middle troposphere
(aerosol and gas injection between 2-6 km)

## Slide 5
AEMet, CSIC and UNAM Deployment at La Palma
Roque de los Muchachos (2400 m): ARCADE Raman Lidar at Cherenkov Telecospe Array + Sun-photometer (AERONET)
El Paso (700 m): Prototype Vaisala CL61 ceilometer
Tazacorte (140 m): Surface SO2, O3, aerosols, MPL lidar (MPLNet+e-profile), all-sky cameras, ZEN radiometer, ash deposition, meteo
Airport (60 m): Vaisala CL51 ceilometer (e-profile), meteo
Fuencaliente (680 m): sun-lunar photometer (AERONET), CHM15k Luff ceilometer (e-profile), all-sky camera, EM27/SUN, DOAS (direct-sun)
Los Llanos (295 m): meteorological sondes
Angeles Alvariño (ship): low-cost air quality products
Mobile records: ash collection and multigas measurements (in collaboration with UNAM)

## Slide 6
DOAS & EM27/SUN Measurements at FUE station
San Antonio (1677) volcano
visitors center, Fuencaliente
Volc. species: HCl, HF, CO2, CO and SO2
Measurement days:
DOAS: 33 (from 10/10 to 10/12 )
EM27/SUN: 59 (from 25/09 to 14/12)
+ 14 (post eruptive)
Days capturing volcanic plume: 21
DOAS &
Optical Fiber
EM27/SUN:
Spectral range: (4000 - 11000 cm-1)
Res: 0.5 cm-1 (OPD max: 1.8 cm)
DOAS: Model Avantes ULS 2048
Spectral range: 270-425 nm
Res: 0.4 nm

## Slide 7
DOAS Measurements and Data Processing
Measurements performed with MobileDOAS software (developed by BIRA-IASB)
Exposition Time: Manually adjusted
Integration time: ~30 sec
QDOAS processing:
Reference: 1 Measured spectrum without volcanic signature & SZA close to 0.0
Settings: Based on Butz et al. (2017)
OClO, BrO (330.6–356.2) nm: too much noise
Conversion of Slant Col. to Vert. Col:
VC_SO2=SlC_SO2/ airmass
with airmass= 1/cos (SZA)
Example of SO2 fit from FUE DOAS solar absorption measurements
Target Gas | Spectral windows (nm) | Interfering gases
SO2 | 312.0-326.8 | O3

## Slide 8
EM27/SUN Data Processing: HCl, HF, CO2, CO
Gas | Spectral windows (cm-1) | Interfering gases
HCl | (5697.0 - 5769.0) (5684.0 – 5795.0 ) * | H2O, CH4
HF_v1 HF_v2 | (7765.0 - 8005.0) (3995.0 - 4043.0) | H2O, CO2 , O2 H2O, HDO, CH4
CO2 | (6173.0 - 6390.0) | H2O, CH4
CO | (4208.7 - 4318.8) | H2O, HDO, CH4
HCl & HF:
*Butz et al., (2017) & Taquet et al., (2023)
Scaling of the lower troposphere (0.630 – 4.0 km) & background contribution neglected
pT files and VMR a priori from MAPs files GGG2014
(factor of 1.00065 with GGG2020)
Volcanic CO2 & CO :
Retrieval with COCCON settings + post-correction to remove the background contribution
Using PROFFAST v2.2 (Hit. 2020 Linelist)

## Slide 9
When IZO data exists: Use of XCO2 IZO to refine the P function
Daily selection of XCO2 data without volcanic contribution (XHCl < 0.002 ppm)
Determination of a P function fitting the selected spectra
(3) Determination of Volcanic CO2 VCD:
ΔXCO2=XCO2–P
CO2VOLC=ΔXCO2 . [O2]/0.20942
Determination of Volcanic CO2 Columns
Based on Butz et al. (2017)
Similar approach for volcanic CO columns

## Slide 10
Examples of Volcanic Plume Detection at FUE and IZO
140km
(At IZO: Days capturing volcanic plume: 9
+ EM27 measurements: 4)

## Slide 11
Volcanic Columns at FUE and IZO: SO2, HCl, HF, CO2, CO
FTIR=EM27/SUN

## Slide 12
Volcanic IFS 125HR Columns at IZO: SO2, HF, HCl, CO
PROFFIT – 2022
(Standard NDACC and optimized products)
Days capturing volcanic plume: 9
Similar results as Popocatépetl volcano (Taquet et al., 2019)

## Slide 13
CO2volc/SO2
Calculation of Ratios from Daily Correlation Plots
HCl/SO2
HF/SO2
COvolc/CO2volc

## Slide 14
Variability of the Volcanic Gas Ratios
Consistency between ratios from EM27/SUN at FUE and IFS125/HR at IZO during the eruption.
Volcanic gas ratios (DCO2/SO2, HCl/SO2, HF/SO2) showed a relationship with a seismic proxy for volcanic activity.
Estimation of Halogen & CO2 emissions during the eruption:
  Total SO2 amount released: 1.84 Mt
  HCl/SO2 mean mass ratio = 0.03+/-0.02
  HF/SO2 mean mass ratio = 0.011+/-0.007
  CO2/SO2 mean mass ratio= 16 +/-6
  Total HCl emissions: 0.055+/-0.040 Mt
  Total HF emissions: 0.021+/0.014 Mt
  Total CO2 emissions: 29+/-11 Mt
  (Mexico city CO2 emissions ~60Mt /year)

## Slide 15
872.55 nm
1020.90 nm
1238.25 nm
1558.25 nm
1636.00 nm
2133.40 nm
2192.00 nm
2314.20 nm
Aerosol Retrievals from EM27/SUN
Spectral Aerosol Optical Depth (AOD)
8 Micro-Windows (very high solar transmission) and continous Langley-plot Calibration at IZO
Aerosol products can be used as proxy for atmospheric chemistry
See poster COCCON-Spain: Towards an Integrated Greenhouse Gas Observation System in Spain
Álvarez et al., submitted to AMTD, 2023
Linear degradation rate of ~0.6%month-1!
Long (3 years) Spectral AOD retrievals at IZO
Validation with co-located AERONET AOD for 870, 1020, 1640 nm (R>0.95, positive bias 1.0-2.5%)
Notes: Slide 15:
The aerosol information is a very useful proxy for atmospheric chemistry and can help us to identify more clearly emission sources in complex conditions.
At IZO, we have developed an approach to retrieve spectral aerosol optical depth from the EM27 sola spectra. To do so, we select eight micro-Windows with high transmission to avoid gas absorptions between 0.8 to 2.3 microns.
Unlike gases, the aerosol retrievals required an absolute calibration of the EM27 spectra, for which we use continuous Langley-plot measurements. Here, the time series of teh calibration coefficient variation with respect to the first valid calibration days, showing a linear degration rate of about 0.6 % per month in the whole study period from 2019 to 2022.
As an example, this is our EM27 AOD for the band of 1020 nm. As you can see, from the comparison with coincident AERONET data used as reference, the agreeement is really robust [robast] with correlation higher tan 95%. In the zoom, for example, we observe as both techniques perfectly capture a volcanic event followed by a mineral dust event.

## Slide 16
EM27/SUN Gas and Aerosol Enhacements
Volcanic gas /aerosols ratios
A volcanic plume from La Palma volcano at IZO (11th October 2021)
∆XCO2/∆AOD = 43.0±4.7 410 ppm/∆AOD
∆XCO/∆AOD = 118.2±11.0 ppb/∆AOD
∆XCO/∆XCO2 = 1.86±0.32 ppb/ppm
∆XCO2 (up to 1 ppm) are comparable to the Kilauea eruption (Hawaii) in 2018, Mt. Etna’s plume (Italy) and the Popocatepetl’s plume.
(Johnson et al., 2020; Butz e al., 2017; Stremme et al., 2023)

## Slide 17
Summary and Outlook
(1) Different tests are still pending, however the excellent agreement between DOAS, EM27/SUN, IFS 125HR points to reliable volcanic SO2, HCl, HF, CO, CO2 measurements!!
(2) Volcanic gas ratios (DCO2/SO2, HCl/SO2, HF/SO2) showed a relationship with a seismic proxy for volcanic activity and allow for determining the order of magnitude of the total gas emissions:
  Total HCl emissions: 0.055+/-0.040 Mt
  Total HF emissions: 0.021+/0.014 Mt
  Total CO2 emissions: 29+/-11 Mt
(3) Low-resolution COCCON instruments are suitable for detecting the aerosol NIR broadband signal and for retrieving precise gas concentrations (multi-parameter capability)

## Slide 18
Many thanks!!!!

## Slide 19
La Palma Volcanic Eruption
Transport to Europe, America and Africa in the middle troposphere
(aerosol and gas injection between 2-6 km)

## Slide 20
AEMet Deployment at La Palma
Air Quality
Aerosol profiling (Transport)
Weather monitoring and forecasting
Research
(aerosols & gases)
IZO WMO-GAW

## Slide 21
Installation of FUE station (La Palma, Canary Islands)
FUE
Tajogaite
Volcano
DOAS &
Optical
Fibber
~14 km
Cumbre Vieja
San Antonio (1677) volcano
visitors center, Fuencaliente
  DOAS instrument (Avantes ULS 2048)
  EM27-SUN (Bruker)
  Ceilometer (CHM), Photometer (CIMEL)
  All-sky camera

## Slide 22
Measurements during La Palma eruption: SO2, HCl, HF, CO2, CO

## Slide 23
CO2 VULC and CO VULC Time series

## Slide 24
Measurements during the La Palma eruption : SO2, HCl, HF, CO2, CO

## Slide 25
Volcanic columns at FUE and IZO: SO2, HCl, HF, CO2, CO

## Slide 26
HCl EM27/SUN (5697.0 - 5769.0) cm-1
HCl IFS 125HR : 12 independent windows in (2727.0 – 2796.5 ) cm-1
(Taquet et al., 2019)
HF EM27/SUN (7765.0 - 8005.0) cm-1 and (3995-4043) cm-1
HF IFS 125HR : (3999.0 – 4003.5) & (4036.5-4041.0) cm-1
(Taquet et al., 2019)
Validation HF & HCl at Popocatépetl: EM27/SUN vs IFS 125HR

## Slide 27
Determination of Volcanic CO columns
ΔXCO=XCOFUE–P
Volcanic CO VCD:
COVOLC=ΔXCO. O2/0.20942

## Slide 28
Variability of the Volcanic Gas Ratios

## Slide 29
References of CO2, SO2, HCl and HF emissions

## Slide 30
WMO-GAW in-situ measurements at IZO: SO2, CO2, CO

## Slide 31
MW (cm-1) | Filter/Detector | Interfering Gases | Fit
2480-2520 | S3&S4, InSb | H2O, CO2, O3, CH4, N2O, SO2 | Scale retrieval for all gases
1120-1180 | S6, MCT | H2O, HDO, CO2, O3, CH4, N2O, SO2, CFC12 | Profile retrieval for SO2, H2O, O3 Scale retrieval for the remaining gases
IFS 125HR SO2 Retrieval Strategies
- Based on Taquet et al. (2019), but they have been optimized and applied consistently to all FTIR sites
- WACCM v6 for all a priori profiles, except for SO2 (on-site information!).
- HITRAN2020 for all gases
  For 1100 cm-1 region the positive constrain using a profile retrieval on a logarithmic scale is CRITICAL, because it avoids SO2 negative concentrations and provides more stable retrievals.
  Total DOFS ≈ 1 (SO2 vertical information is not retrievable!).

## Slide 32
Intercomparison IFS 125HR & Brewer/Pandora at IZO: SO2
Pandora/Brewer (Sep2021 - Feb2022)
Temporal Window: ± 10 min
Difference = FTIR - Pandora/Brewer
Pandora (All SO2>0) | MD (DU) | STD (DU) | R
2500 cm-1 HIT2008 | 0.535 | 1.368 | 0.981
2500 cm-1 HIT2020 | 0.463 | 1.368 | 0.981
1150 cm-1 HIT2008 | 0.085 | 0.697 | 0.995
1150 cm-1 HIT2020 | -0.007 | 0.623 | 0.995
Brewer | MD (DU) | STD (DU) | R
2500 cm-1 HIT2008 | -2.836 | 0.975 | 0.984
2500 cm-1 HIT2020 | -2.897 | 0.978 | 0.984
1150 cm-1 HIT2008 | -3.160 | 0.698 | 0.995
1150 cm-1 HIT2020 | -3.248 | 0.670 | 0.995
Excellent correlation for all SO2 range
HITRAN 2020 provides the best agreement between techniques (1150 cm-1)
Brewer shows a positive bias of 3 DU (SO2 cross section?)

## Slide 33
IFS 125HR HF & HCl Retrieval Strategies
Based on PROFFIT recipes, but they have been optimized.
HF: 2 windows in SA filter (4000.90-4001.05; 4038.85-4039.08) cm-1; interfering gases H2O, O3, CH4 and HF; HITRAN2020 for all gases.
Gas_Setup | Fit | A priori | Vertical Constraint
HF_NDACC | Scale H2O, HF: TP, log, 1e4/300 | WACCM v6 | First and last altitude level clamped
HF_optimized | Scale H2O, HF: TP, log, 1000, 30 | 1E-4 up to 6 km, beyond WACCM v6 | First altitude level free
HCl_NDACC | Scale all, HCl: TP, log, 1000/1000 | WACCM v6 | First and last altitude level clamped
HCl_optimized | Scale all, HCl: TP, log, 100/100 | 1E-4 up to 6 km, beyond WACCM v6 | First altitude level free
HCl: 4 windows in SC filter (2727.73-2727.83; 2775.60-2775.90; 2821.40-2821.75; 2925.75-2926.10) cm-1; interfering gases H2O, HDO, O3, N2O, CH4, HCl, and OCS; HITRAN2020 for all gases.
HF_optimized

## Slide 34
Gas_Setup | Median Residues (STD) [au] | Median Iterations (STD) | Median DOFS (STD)
HF_NDACC | 128588 (674735) | 5 (3.46) | 1.80 (0.32)
HF_optimized | 49725 (166614) | 6 (2.71) | 2.73 (0.27)
HCl_NDACC | 13684 (52165) | 3 (1.11) | 2.03 (0.33)
HCl_optimized | 11450 (13367) | 4 (1.78) | 3.33 (0.33)
IFS 125HR HF & HCl Retrieval Strategies
Averaging Kernels, a priori and retrieved VMR profiles
Performance
HF_optimized
HCl_optimized

## Slide 35
Summary of IFS 125HR Retrieval Strategies
Gas Setup | Filter/Detector | Mw (cm-1) | Interfering Gases | Fit
SO2 | S3&S4, InSb | 2480-2520 | H2O, CO2, O3, CH4, N2O, SO2 | Scale retrieval for all gases
SO2 | S6, MCT | 1120-1180 | H2O, HDO, CO2, O3, CH4, N2O, SO2, CFC12 | Profile retrieval for SO2, H2O, O3 Scale retrieval for the remaining gases
HF | SA, Ingas | 4000.90-4001.05; 4038.85-4039.08 | H2O, O3, CH4 and HF | Scale H2O, HF: TP, log, 1000, 30 Vert. Constraint: First altitude level free
HCl | SC, InSb | (2727.73-2727.83; 2775.60-2775.90; 2821.40-2821.75; 2925.75-2926.10) | H2O, HDO, O3, N2O, CH4, HCl, and OCS | Scale all, HCl: TP, log, 1000/1000 Vert. Constraint: First and last altitude level clamped

## Slide 36
872.55 nm
1020.90 nm
1238.25 nm
1558.25 nm
1636.00 nm
2133.40 nm
2192.00 nm
2314.20 nm
Aerosol Retrievals from EM27/SUN
Spectral Aerosol Optical Depth (AOD)
8 Micro-Windows (very high solar transmission) and continous Langley-plot Calibration at IZO
Aerosol products can be used as proxy for atmospheric chemistry (CO/SO2: 2 ranges = 2 different sources Volcanic CO or GHG/biomass burning (due to lava flows))
See poster COCCON-Spain: Towards an Integrated Greenhouse Gas Observation System in Spain
Linear degradation rate of ~0.6%month-1!
Validation with co-located AERONET AOD for 870, 1020, 1640 nm
Excellent correlation for all the AOD range
EM27/SUN AOD shows a positive bias between 1-2.5%