## Slide 1
GHG observations at the COCCON Tsukuba site
Matthias Max Frey, Isamu Morino, Hirofumi Ohyama, Astrid Müller et al.

## Slide 2: Ground-based remote sensing networks at NIES
TCCON & NDACC
  High-resolution spectrometer
  Gold standard for satellite validation
  Capable of profile retrieval
COCCON
  Small, portable spectrometer (EM27/SUN)
  Low infrastructure demands
    Various applications

## Slide 3: COCCON Tsukuba site

## Slide 4: Instrumental stability
Verification of instrumental stability using different metrics
  Instrumental line shape (ILS) measurements
  Xair timeseries
  Calibration w.r.t. COCCON reference instrument in Karlsruhe
COCCON Tsukuba instrument (SN063) remarkably stable since 2016
ILS timeseries
Xair timeseries

## Slide 5: Instrumental stability
Calibration w.r.t. COCCON reference instrument (SN037) in Karlsruhe
  Performed January 2016
    Instrument specific calibration factors: XCO2 – 1.0003, XCH4: 1.0001
  EM27 Travel Standard (SN039) visited Tsukuba April 2022
  Check calibration w.r.t. reference instrument using Travel Standard
    Instrument specific calibration factors: XCO2 – 1.0003, XCH4: 1.0008
COCCON Tsukuba instrument (SN063) remarkably stable since 2016
Comparison SN037 – SN039 Karlsruhe
Comparison SN063 – SN039 Tsukuba

## Slide 6: COCCON timeseries

## Slide 7: GOSAT series validation: GOSAT NIES v02.91
± 2° coincidence criterion
COCCON Measurements ± 30 min of overpass
XCO2 bias: 1.1 ppm
XCO2 STD: 2.4 ppm
Slight GOSAT XCO2 high bias expected as coincidence criterion includes the densely populated Kanto plain

## Slide 8: GOSAT series validation: GOSAT-2 FP v02.00
± 2° coincidence criterion
Higher number of coincidence observations compared to GOSAT
For XCO2, XCO, and XCH4 observed biases are similar to biases seen by the GOSAT validation team for TCCON comparison

## Slide 9: OCO-2 / OCO-3 validation
± 2° coincidence criterion
OCO-3 data screened for Tokyo SAMs
Only overpasses including over 500 footprint pixels with quality flag == 0 used
OCO-2
bias 0.1 ppm,
STD 0.6 ppm
OCO-3
bias 0.0 ppm,
STD 1.1 ppm

## Slide 10: TROPOMI XCH4 validation
Only TROPOMI overpasses with quality flag > 0.5 for at least 100 footprints used
TROPOMI bias 9 ppb, STD 7ppb
Bias as well as STD are well within the TROPOMI mission requirements

## Slide 11: TROPOMI XCO validation
Here 0.5° coincidence criterion used, this still includes most of Tokyo
Compared to 2° criterion, the bias decreases, on the edge of not being significant on the 1-σ level
Also tested 0.2° criterion and min pooled data for COCCON No significant difference
Bias as well as STD are well within the TROPOMI mission requirements

## Slide 12: Ship-borne EM27/SUN observations

## Slide 13: Research vessel Mirai cruises 2021/2022
NIES and Heidelberg University collaboration
Partly harsh environmental conditions
  Wave heights up to 10 m
  Strong winds
MR21-1
  February 13 – March 22 2021
MR21-6
  December 18 2021 – January 13 2022
  Software update to enable remote control
    Observations even when outside access prohibited
MR21-1
MR21-6

## Slide 14: First cargo ship-based XCO2, XCH4, and XCO measurements with a semi-automatic EM27/SUN
EM27/SUN
Phase 1: Technical feasibility (successful)
Test under “real” conditions 6/2022 – 9/2022
Remote control via LTE router
Phase 2: Operational measurements along
major emission hotspots of Japan (scheduled for September 2023)
 dataset for the validation of
obs. XCO2, XCH4, XCO, NO2
GOSAT series, OCO-2/3, TROPOMI retrievals
models
Vehicle carrier “Nichiyu Maru” (Kagoshima Senpaku Co., Ltd.)
International collaboration: NIES, Japan (Astrid Müller, Matthias Max Frey, Hiroshi Tanimoto, Isamu Morino, Shin-Ichiro Nakaoka), Heidelberg University, Germany (Ralph Kleinschek, Ken von Buenau, André Butz)
Remote control via LTE router and camera from office/home
Setup location
Google Maps, Map data ©2021
Return trip:
1 week
Slide courtesy of Astrid Müller

## Slide 15: Spare slides

## Slide 16: Instrumental challenges
Vibrations
Spikes
Fourier Transformation
Retrieved Xgas for sample day
Could normally be mitigated

## Slide 17: Results MR21-1 [Butz et al., 2022, FRS]
EM27 Xgas timeseries + CAMS model + TROPOMI satellite (only CO)
Lack of measurements in the first half due to rough weather conditions
Constant offset between CAMS and EM27 for XCO2 and XCH4
XCO/XCO2 enhancements at the end
Good agreement between EM27 and CAMS enhancement ratio