## Slide 1
Bringing FTIR measurements into GRUAN
The ground-based FTIR remote sensing technique
Generation of error estimates
Example: The water vapour products within the project MUSICA
Progress in EU FP7 project NORS
Assets of the Technique:
  high quality,
  profiling capability,
  high measurement frequency
Notes & Discussion Points
M. De Mazière, M. Schneider, J. Hannigan

## Slide 2
A ground-based solar-viewing FTIR remote-sensing installation ~$500k
Often the observations are made at remote sites (mountains, polar regions, etc.): the whole experiment can be mounted in a standard shipping container with electricity, heating, internet connection, etc.
Most stations use a Bruker IFS 125HR: very high quality and commercially available. Dimensions: 200cm x 300cm; Price: ~ 300 k€
Furthermore a precise solar tracer system is required (e.g., Gisi et al. AMT 2011)
Instrument status is monitored via cell measurements (commonly manufactured)
Notes: Automatic ; remote control

## Slide 3
Simultaneous observation at high spectral resolution in wide spectral bands yield absorption signatures of many trace gases (required)
H2O HDO O3 N2O CH4 HNO3 CCl2F2 CCl3F CHClF2 COF2 ClONO2 ClO NO NO2 HCl C2H6 HF HCN C2H2 CO CO2 OCS NH3 COCl2 N2
CO2
Gb FTIR measurements within NDACC
Spectral Resolution:
0.0035-0.002 cm-1 required for profiling using presssure (Lorentz) broadening effect.
SNR:
300 – 2000 RMS
Spectral Range:
750–4500 cm-1
Data Rate:
Daily but many sites all daylight clear-sky time

## Slide 4: TCCON: Total Carbon Column Observing Network
similar instruments
similar data analysis principles
But
  In near-infrared
  More prescriptive procedures for data acquisition
  Focus on high-precision column-averaged dry-air volume mixing ratios of greenhouse gases CH4, CO2, N2O, H2O, CO
  1 single data processing S/W
8000 7000 6000 5000 4000
wavenumber (cm-1)

## Slide 5: Global FTS Stations
Eureka | 80 | 274
Ny_Alesund | 79 | 12
Thule | 77 | 291
Kiruna | 68 | 20
Sodankyla | 67 | 27
Poker_Flat | 65 | 213
Harestua | 60 | 11
St_Petersburg | 60 | 30
Yekaterinburg | 57 | 60
Tomsk | 57 | 85
Bialystok | 53 | 23
Bremen | 53 | 9
Bratts_Lake | 50 | -104
Karlsruhe | 49 | 8
Paris | 49 | 2
Orleans | 48 | 2
Garmisch | 47 | 11
Zugspitze | 47 | 11
Jungfraujoch | 47 | 8
Park_Falls | 46 | 270
Moshiri | 44 | 142
Egbert | 44 | 280
Rikubetsu | 44 | 144
Toronto | 44 | 281
Boulder | 40 | 255
Barcroft | 38 | 242
Lamont | 37 | 263
Tsukuba | 36 | 140
Table_Mtn | 34 | 242
Kitt_Peak | 32 | 248
Wollongong | -34 | 151
Lauder | -45 | 170
Izana | 28 | 344
Mauna_Loa | 20 | 204
Mexico_City | 19 | -99
Altzomoni | 19 | -99
Addis_Ababa | 9 | 39
Paramaribo | 6 | 305
Ascension | -8 | -14
Darwin | -12 | 131
Reu_Maido | -21 | 55
Reu_St_Denis | -21 | 55
Syowa_Station | -69 | 40
Arrival_Heights | -79 | 167
~Tropical
Mid-Latitude
Arctic
Antarctic
Notes: Lat °N/ lon °E in Tables
Developing countries

## Slide 6: Many Common Members in TCCON & NDACC MUSICA is a subset of NDACC groups…
Shared meetings for several years, common experience, problems & solutions
Institute | NDACC Sites | TCCON Sites | MUSICA
JPL | 1 | 3+ | 
U. Wollongong | 1 | 1 | 1
KIT Karl. | 4 | 1 | 4
U. Bremen | 4 | 3 | 1
BIRA | 1 | 1 | 
NIES | 1 | 1 | 1
KIT Gar. | 1 | 1 | 
NIWA | 2 | 1 | 2
U.T. | 2 | 1 | 1
U Liege | 1 |  | 1
 | 17 | 13 | 11

## Slide 7: Instrumentation / Data Products
 | TCCON | IRWG | MUSICA
Instrument | 125HR (Bruker) | By spec. (Bruker) | By spec. (Bruker)
OPD* | 45cm | 250cm (max) | 250cm (max)
Region** | Near-IR | mid-IR | mid-IR
Recording | DC | DC/AC | DC/AC
Bandwidth | 3900-15000 | 700-4500 | 700-4500
Detectors | InGaAs/Si | InSb/MCT | InSb/MCT
Retrieval | NLLS / Scale of apriority | Full Optimal Est | Full Optimal Est
Species | CO2 (CH4, N2O, CO) | 10 primary + | H2O
Product | Column/DAMF | Column/Profile | Column/Profile
*Low resolution instruments (~1 cm) are being developed (ie lower cost)
*Possible MIR/NIR Instrument has been proposed

## Slide 8: L1 (spectra)  L2 (columns ; vertical profiles)
Requires forward model :
radiative transfer model of sunlight through the atmosphere including absorption, emission and scattering processes.
Solar absorption => direct absorption is dominant
Spectroscopic data of atmospheric constituents
+ inverse model:
For vertical profile retrieval : ill-posed problem
NLLS fitting + Regularisation or Optimal Estimation Method
Actual status in NDACC: 2 standard algorithms (inter-compared)
Actual status in TCCON: 1 single algorithm and central data processing verification

## Slide 10
Srand
Ssyst
Provide averaging kernel A  smoothing error
Model error is neglected
Notes: Model error is neglected

## Slide 11
Measurement noise
background slope
background curvature
differential wavenumber shift
single wavenumber shift
independent wavenumber shift
empirical apodization function
empirical phase function
solar line shift
solar line strength
simple phase error
zero level offset
interfering species
channel parameters
temperature profile
target gas absorption line(s) intensity
target gas absorption line(s) air broadened line half-width
retrieved gas absorption line(s) intensity
retrieved gas absorption line(s) air broadened line half-width
other possible line parameters:
  self broadening
  lower state energy
  temperature dependence exponent
  pressure shift
  Galatry Beta
  line mixing parameters
  S-DV parameters
solar pointing
Optimal Estimation in Practice & Error estimation of State vector 3/4
Error sources:

## Slide 12
The sensitivity of x̂ on a given bi is minimized by early choices in the retrieval process (eg spectral region).
  This is made homogeneous across the network by recent efforts to use identical retrieval parameters at all sites.
The best estimate of Sbi may be
  Site and instrument dependent
  Needs to be physically based,
  May require some testing to determine,
  Procedure to evaluate it needs to be ‘homogeneous’ across all sites.
Error analysis homogenization effort in progress (recent NDACC/NORS Error Analysis Workshop NCAR Jan 2013)
Aim:
provide common S/W package for calculating uncertainty budget for each data point, to be reported in the data file (random part and systematic part).
Optimal Estimation in Practice & Error estimation of State vector 4/4

## Slide 13
site contributing to MUSICA
MUSICA (MUlti-platform remote Sensing of Isotopologues for investigating the Cycle of Atmospheric water) combines NDACC ground-based FTS observations and IASI / METOP observations (and in-situ observations for validation purposes).
Example: The project MUSICA: consistent ground- and space-based water vapour products
Acknowledgement: MUSICA is funded by the European Research Council under the European Community's Seventh Framework Programme (FP7/2007-2013) / ERC Grant agreement n° 256961.
Schneider and Hase (2011); Schneider et al. (2012)
The MUSICA project team (M. Schneider et al.) at the Karlsruhe Institute of Technology (KIT), Karlsruhe, Germany, and the Agencia Estatal de Meteorología (AEMET), Santa Cruz de Tenerife, Spain
http://www.imk-asf.kit.edu/english/musica
+

## Slide 14
We measure high resolution broadband spectra. For the analysis we select spectral regions where the target species has well isolated absorption signatures:
MUSICA‘s ground-based FTIR spectral windows
Example of the spectral windows used for H216O and HD16O retrievals:

## Slide 15
Vertical Sensitivity & Error assessment for MUSICA‘s g-b FTIR water vapour product
Data quality is well assessed for each individual observation at all stations. For more details see Schneider et al. (2012), Sect. 4.1: „Characterisation of product type 1: Optimally estimated H2O profiles”
Example at Izana

## Slide 16
Total number of available water vapour profiles: ≈15000
Spectra submitted by PI then centrally processed at KIT
Representative for ten globally distributed sites, :
NH, SH, polar, mid-laitudes, (sub)-tropics, land surface, ocean surface, lowland, high mountains, etc.
Current state of MUSICA gb FTS water vapour dataset: 10 stations, data since mid 90s, …
http://www.imk-asf.kit.edu/english/musica

## Slide 17
Asset (1): very high quality as documented by retrieved O2 and pressure correlations
differential absorption principle
→ „self calibrating“
→ the gb FTS technique can produce very precise long-term data sets
The plots are courtesy by E. Sepúlveda

## Slide 18
lower troposphere (3 km):
Asset (2): „profiles“ of high quality, example study 2005-2009, FTS vs. Vaisala RS92
Schneider et al., AMT, 2010

## Slide 19
High measure-ment frequency is important for water vapour, because of the high variability!
Asset (3): high measurement frequency, example MOHAVE-2009 campaign
Acknowledgement
FTIR spectra and RS92 data were provided by G. Toon, J.F. Blavier, and T. Leblanc, JPL, California, USA

## Slide 20
Progress in NORS (EU FP7 project, Nov. 2011- mid 2014):
Objective: tailor NDACC FTIR, LIDAR, MICROWAVE, and UVVIS DOAS products to the needs of supporting the quality assessment of the GMES (Copernicus) Atmospheric Service.
In progress
Rapid data delivery within 1 month
Full characterisation of products (uncertainties, sensitivities, horizontal and vertical averaging kernels, uncertainties, …)
Data user guide
Data uncertainties guide
Data consistency checks (whenever redundancy, and versus satellite data
Methods for data intercomparisons and data integration

## Slide 21
Summary
The ground-based FTIR remote sensing technique offers high precision and long-term stability (cf. cell measurements)
Existing networks are in place and adaptable for evolving requirements
Working towards more homogeneous data products, furthered by
  Instrumentation standards,
  Certification protocol
  Consistent retrieval parameters,
  Consistent error analysis.
Water vapour (and HDO/H2O) profiles of a carefully documented quality are produced within the project MUSICA and available for ten globally distributed sites (for some stations dating back to the mid 90s)
Valuable reference dataset due to combination of high quality, long-term availability, profiling capability, and high measurement frequency
NDACC data are delivered in GEOMS compliant HDF files including metadata, and uncertainties; all data are referenced to SI units
Ancillary data (surface temperature, pressure water vapor profile & column are included)
Data already widely used for satellite and model validation

## Slide 22
Issues raised in GRUAN:
Central storage of raw (L1) data,
  Not implemented (but all PI’s save their raw data)
  ‘Level’ of raw tbd (eg. spectrum or interferogram?)
  Depending on level & measurement frequency, data rate could be to a Gb/day
Quantified uncertainties with every data point
  Desired by all - in progress
Traceability
  As in HITRAN, NCEP – OK
  TCCON includes calibration to in-situ aircraft data
  Further calibration may be required by GRUAN
  HDF file does not include full traceability information
Central processing,
    in place for MUSICA, not wider NDACC, but possible
    is an implemented part of TCCON but not standard
Homogeneity of the measurements across the network:
  Active, in everyone’s interest – how to prove they are not?
Redundant observations:
  Partly dealt with in NORS for ozone, CO and CH4, in MUSICA for H2O

## Slide 23
EXTRA SLIDES

## Slide 24
For details please refer to the recent publications on the MUSICA dataset
Schneider, M., S. Barthlott, F. Hase, Y. González, K. Yoshimura, O.E. García, E. Sepúlveda, A. Gomez-Pelaez, M. Gisi, R. Kohlhepp, S. Dohe, T. Blumenstock, A. Wiegele, E. Christner, K. Strong, D. Weaver, M. Palm, N.M. Deutscher, T. Warneke, J. Notholt, B. Lejeune, P. Demoulin, N. Jones, D.W.T. Griffith, D. Smale, and J. Robinson:
Ground-based remote sensing of tropospheric water vapour isotopologues within the project MUSICA,
Atmos. Meas. Tech., 5, 3007-3027, 2012.
Schneider, M. and F. Hase:
Optimal estimation of tropospheric H2O and δD with IASI / METOP,
Atmos. Chem. Phys., 11, 11207-11220, 2011.

## Slide 25
Ground-based FTS retrieval principle
We invert the spectra by an optimal estimation method.
Minimise the cost function:
measurement information + a priori information
Rodgers (2000)

## Slide 26
Ground-based FTIR: an important reference for validating satellite sensors
(3): Gb FTIR can measure quasi continuously (during daytime), essential for proper validation:
(1): High quality data
(2): Gb FTIR and satellite sensor kernels overlap, example FTIR and IASI:
IASI overpass

## Slide 27
Due to the pressure broadening effect very high resolution spectra contain information about the absorbers vertical distribution
In the middle infrared the pressure broadening determines the line shape between the Earth‘s surface and about 40 km altitude.
Spectra analysis: information on the absorbers‘ vertical distribution
O3
Example for O3:

## Slide 28
Limitation of the FTS technique: observation only exists for clear sky conditions
Estimated clear sky dry bias at the subtropical Izaña Observatory:
Schneider et al., AMT, 2010

## Slide 29
An extensive long-term multi-instrument intercomparison at the Izaña Observatory documents the high precision of the FTIR total water vapour column data.
Theoretical and empirical precision estimate: 0.5 – 1.5%
Quality of H2O total column amounts
Schneider et al., AMT, 2010

## Slide 30
NDACC: Network for the Detection of Atmospheric Composition Change
TCCON: Total Carbon Column Observing Network
There are two global networks measuring high resolution solar absorption spectra in the infrared applying very high quality instrumentation
Global ground-based FTIR networks

## Slide 31
Typical averaging kernels for MUSICA‘s gb FTIR water vapour product, example Izana

## Slide 32
middle troposphere:
Schneider et al., AMT, 2010

## Slide 33
upper troposphere:
Schneider et al., AMT, 2010

## Slide 34
central storage of raw data,
quantified uncertainties with every data point,
traceability,
central processing,
homogeneity of the measurements across the network,
redundant observations.

## Slide 35
MUSICA (MUlti-platform remote Sensing of Isotopologues for investigating the Cycle of Atmospheric water) combines NDACC ground-based FTS observations and IASI / METOP observations (and in-situ observations for validation purposes).
Example: The project MUSICA: consistent ground- and space-based water vapour products
http://www.imk-asf.kit.edu/english/musica
Acknowledgement: MUSICA is funded by the European Research Council under the European Community's Seventh Framework Programme (FP7/2007-2013) / ERC Grant agreement n° 256961.
Schneider and Hase (2011); Schneider et al. (2012)
site contributing to MUSICA
The MUSICA project team (M. Schneider et al.) at the Karlsruhe Institute of Technology (KIT), Karlsruhe, Germany, and the Agencia Estatal de Meteorología (AEMET), Santa Cruz de Tenerife, Spain

## Slide 36
C2H6
Simulation
Notes: Zoom again to 5 cm-1
Separate absorptions to individual gases
Note difference hcl (narrow/strat) and water (broad/trop)
Top curve is absorptions in solar chronosphere
Bottom (red) is measured spectrum (previous slides)
2nd from bottom is sum of all calculated single gas spectra