## Slide 1
NH3 and NOx emissions from CAFO soils, and Structure Functions measured by CU mobile SOF during FRAPPE and ARISTO16
Rainer Volkamer & Natalie Kille
Department of Chemistry and Biochemistry & Cooperative Instituted for Environmental Sciences (CIRES), University of Colorado at Boulder
Instrumentation: CU SOF
Quantify emission fluxes of NH3, NOx, C2H6 from Oil & Ag near Greeley, CO
Comparison with NEI2011 & structure functions
Outlook: Airborne SOF

## Slide 2
Natalie Kille
Sunil Baidar
Philip Handley
David Thomson
Roman Sinreich
Ivan Ortega
Jim Hannigan, Gabi Pfister (NCAR)
Frank Hase (KIT)
Owen Cooper (NOAA)
Dan Bon (CDPHE)
Pavel Romashkin (NCAR/EOL/RAF)
CAFO emissions
BB emissions
Excess CH4 source
apportionment
Poster: Kille et al. Separation of methane emissions from biogenic sources and natural gas …

## Slide 3
Research drives – FRAPPE 2014
RD Date Description
1 07/21 Sampling at Magnum CAFO
2 07/28 Urban emission around Denver
3 08/01 Urban emission around Denver
4 08/02 Urban emission around Denver
5 08/04 Regional outflow and CAFO
6 08/06 Regional outflow
7 08/08 Regional within Boulder County
8 08/09 Regional outflow
9 08/11 Regional
10 08/12 Various farms around Greeley
11 08/13 Various farms around Greeley
12 08/15 Regional within Boulder County
13 08/16 Overflight, BAO tower
14 08/18 Morning mountain upslope flow
15 08/18 Evening mountain upslope flow
16 09/03 Urban emission around Denver
Boulder
Denver
Ft. Collins
Greeley
Front Range Air Pollution and Photochemistry Experiment

## Slide 4: CU mobile SOF: emission flux & chemistry
UV-VIS & mid-IR measurements of columns are independent of PBLH

## Slide 5
Baidar et al., 2016 AMT; U.S. Patent Pending
Digital mobile solar tracker
Access to the Euler Angles of the sun.
Active control to correct for vehicle motion
 Less time adjusting & more time measuring

## Slide 6
Fit Examples: UV-vis

## Slide 7
Fit Examples: mid infrared
CO
NH3
%rms = 1.9
4.02 x 1017 molec/cm2

## Slide 8
Research drives – spatial variability
IASI
CriS
TES
TEMPO
OMI
OMI
IASI
CriS
TES

## Slide 9
Case Study – RD11
Site 1 – Dairy
Site 2 – Beef
Site 3 – Sheep
Site 4 – Dairy
Site 5 – Dairy
Wind averaged over
Full PBLH
Half PBLH
Lowest level
NH3 NO2

## Slide 10
NH3 Emission Factors:
Beef: 12.0 ± 2.8 g hr-1 head-1
Dairy: 11.4 ± 3.5 g hr-1 head-1
NOx Emission Rates:
Site 2: 7.3 ± 2.9 kg km-2 hr-1 or 18.6 kg hr-1
Emission Flux
11.8 ± 2.1 g hr-1 head-1

## Slide 11
Comparing NH3 flux to the NEI 2011
Kille et al., 2017 AMT
Weld County:
535 766 cattle
10440 km2
0.63 kg km-2 hr-1
NEI – avg NH3 ERate:
0.36 kg km-2 hr-1
(all sources)
1.8
NH3 EF = 11.8 g hr-1 head-1
(12.9% of cattle population in Weld County were probed)
Remote Study area:
224 469 cattle
414 km2
6.39 kg km-2 hr-1
NEI – avg NH3 ERate:
0.73 kg km-2 hr-1
(all sources)
8.8
Ratio Meas/NEI:
~100-600 kg/hr

## Slide 12
Comparing NOx flux to the NEI 2011
~18.6 kg/hr
Kille et al., 2017 AMT
Weld County:
535 766 cattle
10440 km2
0.018 kg km-2 hr-1
NEI – avg NOx ERate:
0.17 kg km-2 hr-1
(incl. traffic)
+11%
Site 2: 18.6 kg hr-1 or 0.34 g hr-1 head-1
(comprises 10% of cattle population in Weld County)
Remote Study area:
224 469 cattle
414 km2
0.18 kg km-2 hr-1
NEI – avg NOx ERate:
0.15 kg km-2 hr-1
(incl. traffic)
+120%
Additional NOx
from CAFO Soils:

## Slide 13: Structure functions & satellites
50% variability at <1.6km
90% variability at <5.6km
TES
50%
90%
IASI, CrIS
>95%
  NH3 – IASI (12 x 25 km2), TES (5.3 x 8.5 km2), CrIS: currently resolve 5-10% of the NH3 VCD variability in the Colorado Front Range
NO2 - TEMPO (future: 2 x 4.5 km2): will be able to resolve ~50% of the NO2 VCD variability in the Colorado Front Range

## Slide 14: ARISTO2016: CU airborne SOF
Potential future applications include study of biomass burning emissions and plume processing
~5 TgN/yr
Baidar et al., 2016 AMT
Kille et al., 2017 AMT
Postdoctoral openings:
Airborne SOF & biomass burning fluxes
Notes: Animals 32 (24 – 40)
Sea 13 ( 8 – 18) (largest natural source)
Soils 10 ( 6 – 45)
Fertilizer 9 ( 5 – 10)
Biomass 5 ( 1 – 9)
Other 6

## Slide 15: Conclusions
The observed NH3 EF (11.8 ± 2.1 g hr-1 head-1) is compatible with the upper range of literature values (Kille et al., 2017). Emissions of NH3 from cattle are underestimated by a factor 1.8-8.8 (NEI 2011).
NOx emissions from CAFO soils account for 1.2% of the N-flux.
This NOx source is currently missing in models, and becomes increasingly important as other NOx sources continue to decrease. It has potential to add between 10% (county) and 120% (remote) to the NOx burden. Missing NOx sources are relevant because O3 chemistry is NOx limited in remote areas where CAFO are located.
Future - airborne SOF: many molecules (CO, C2H6, C2H2, CH3OH, HCOOH, HCHO, CHOCHO, NH3, HCN, NO, NO2, HONO, HNCO?, etc.)
Funding: CDPHE, NSF, CIRES, KIT
rainer.volkamer@colorado.edu

## Slide 16: Former Volkamer group members
Ivan Ortega
Scientist
Eleanor Waxman
NRC fellowship/NIST
Ryan Thalman, tenure track faculty
Snow College, Richfield, UT
Hilke Oetjen
NASA-JPL
Christopher Kampf, Junior Group
MPI Chemistry, Germany
Faculty
PI position
Postdoc
National
Laboratory
Postdoc
Industry
Postdoc
University
Sean Coburn, Siyuan Wang
Postdoc CU/NIST, UMichigan
Sunil Baidar
CIRES-NOAA/Ball Aerospace

## Slide 17: Food, Energy & Environment
Global budget of NH3
  75 (50 – 128) TgN/yr (Schlesinger & Hartley, 1992, Biogeochemistry)
  65 (45 – 85) TgN/yr (Sutton et al., 2013, RSTP)
“Despite the fact that NH3 at its current levels is a major threat to the environment and human health, relatively little is known about its total budget and global distribution.” (Dammers et al., 2016, ACP)
Source: Google Images
~32 TgN/yr
~13 TgN/yr
~10 TgN/yr
~9 TgN/yr
~5 TgN/yr
Notes: Animals 32 (24 – 40)
Sea 13 ( 8 – 18) (largest natural source)
Soils 10 ( 6 – 45)
Fertilizer 9 ( 5 – 10)
Biomass 5 ( 1 – 9)
Other 6

## Slide 18
NH3
NOx
physicalgeography.net