## Slide 1
Developing Fuel-Based Inventories of Mobile Source and Oil & Gas Emissions for Colorado
Brian C. McDonald, Ph.D.
CU/NOAA: Stuart McKeen, Yuyan Cui, Ravan Ahmadov, Si-Wan Kim, Jeff Peischl,
Tom Ryerson, Gregory Frost, Michael Trainer
Undergraduate Students: Alan Gorchov Negron (Brown Univ.), Justin DuRant (Univ. South Carolina)
Acknowledgments: NCAR SOARS and NOAA Hollings Scholarship programs
FRAPPÉ Science Team Meeting: May 2, 2017

## Slide 2
Recent Studies Suggest Overestimate in U.S. NOx Emissions
Mobile Sources
Oil & Gas Development
Industry
  DISCOVER-AQ (2011): Mobile source NOx high by 51-70% in the National Emissions Inventory (NEI) 2011 (Anderson et al., Atmos. Env. 2014)
  SEAC4RS (2013): Industrial and mobile source NOx high in the NEI, 30-60% reductions needed (Travis et al., Atmos. Chem. Phys. 2016)
  UBWOS (2012-13): Oil & gas NOx in the Uintah Basin, UT high by factor of ~4x in the NEI (Ahmadov et al., Atmos. Chem. Phys. 2015)

## Slide 3
Research Objectives
Construct a fuel-based inventory of on-road emissions
  Focus on NOx, but CO and VOCs can also be estimated
  Evaluate in an atmospheric model
Construct a fuel-based inventory of oil & gas emissions
  Evaluate with “top-down” emissions derived by aircraft data
Are NOx emissions in the NEI overestimated in Colorado, as reported elsewhere from recent field campaigns?

## Slide 4
Building an Alternative Bottom-Up Vehicle Emissions Inventory
State-level taxable gasoline and diesel fuel sales reports
Public and annual
Map on-road CO2 emissions
Using traffic count data
Basis for scaling co-emitted combustion byproducts
DENVER
See McDonald et al. (J. Geophys. Res. 2014)
for more details
Emissions = Activity (kg fuel) x Emission Factor (g/kg fuel)

## Slide 5
Use of Roadway Studies for Emission Factors
Emissions = Activity (kg fuel) x Emission Factor (g/kg fuel)
Roadside monitoring data
Measures in-use vehicles
Captures high-emitters
Regulatory models typically rely on chassis dynamometer tests
Univ. of Denver FEAT

## Slide 6
Long-Term Trends in U.S. On-Road NOx Emission Factors
Figure updated from McDonald et al. (J. Geophys. Res. 2012)
Diesel EF high
within ~20%
Gasoline EF high
by factor of ~2
(MOVES EF are default values)

## Slide 7
Difference in Total U.S. NOx Emissions (Fuel-Based – MOVES)
This Study: -20%
Travis et al. (2016): NEI 2011 emissions of NOx too high by ~50%
Southeast Nexus Study 2013

## Slide 8
Comparing Fuel-Based Inventory and NEI/MOVES in Regional Model
Downtown Atlanta
Nashville
McDonald et al. (in prep.)

## Slide 9
Reducing NOx Emissions Improves O3 Models
Bias in summer 2013 O3 exceedance days
(>70 ppb) modeled with NEI 2011 vs. AQS data
McDonald et al. (in prep.)
 FIVE is worse
FIVE is better 

## Slide 10
Fuel-Based Estimate of Oil & Gas NOx Emissions
  Exploration
  e.g. drilling, fracturing, trucking
  Off-road diesel fuel (EIA)
  Production
  e.g. dehydrators, heaters, compressors
  NG on-site fuel (EIA)
  NG Processing Plants
  CO2 emissions reported at facility level (EPA)
EPA Oil & Gas Tool
+
Literature Review
Continuous Emissions Monitoring (CEMS)
Emissions = Activity (kg CO2) x Emission Factor (g/kg CO2)

## Slide 11
Fuel-Based Inventory of Oil & Gas Emissions Scalable Across U.S.
Gorchov Negron et al. (in prep.)
Well-level production, drilling data used to spatially allocate emissions
Evaluate with
aircraft-derived
“top-down” emissions

## Slide 12
Comparison of Top-Down and Bottom-Up Emissions in O&G Basins
NEI high by ~2.5x on average, fuel-based inventory low by ~30%
Gorchov Negron et al. (in prep.)

## Slide 13
Modeling O3 in Uintah Basin during Wintertime
Observations Bottom-up (NEI11) Top-Down Zero Oil & Gas
O&G NOx emissions in NEI11 high by ~4x, VOC emissions low by ~2x
Ahmadov et al. (Atmos. Chem. Phys. 2015)

## Slide 14
In Denver Front
Range Counties
On-Road
Fuel-Based 27 000 mt/y
NEI14 38 500 mt/y
(+43%)
Oil & Gas
Fuel-Based 9 400 mt/y
NEI14 17 200 mt/y
(+83%)

## Slide 15
Summary
Developed fuel-based inventory for on-road and oil & gas sectors
    Similar methodology employed based on energy statistics, in-situ measurements (where available), and spatial surrogates
  NOx emissions evaluated with field intensive measurements
    Evidence for overestimate in on-road gasoline NOx in NEI →
    over-prediction of O3 exceedance events in Eastern U.S.
    Evidence for overestimate in oil & gas NOx in NEI, but varies by basin
  Compared to the fuel-based inventory, NOx emissions in the NEI are higher for the on-road and oil & gas sectors in Colorado