## Slide 1
Anthropogenic Sources of non-OH Oxidants of SO2
Lee Mauldin
Chris Cantrell
Department of Atmospheric and Oceanic Sciences, University of Colorado, Boulder
and the FRAPPE Science Team

## Slide 2
SUOMI – SUlfuric OH and MSA Instrument
Hydroxyl (OH) – Primary oxidant in the Earth’s atmosphere
Sulfuric Acid (H2SO4) – Oxidation product of SO2. Important in aerosol formation and growth
Methane Sulfonic Acid (MSA) – Oxidation product of dimethyl sulfide (DMS)
Utilizes Nitrate Chemical Ionization – Mass Spectrometry

## Slide 3
HNO3 → NO3-
NO3- + H2SO4 → HNO3 + HSO4-
NO3- + (CH3)SO3H → (CH3)SO3-
Ionized
Mass 99 for H34SO4- (OH)
Mass 97 for HSO4-
Mass 95
Mass 62
[OH] = C
H34SO4-
NO3-
OH is measured by first converting it to H234SO4 via:
OH + 34SO2 → H34SO3
H34SO3 + O2 → 34SO3 + HO2
34SO3 + 2H2O → H234SO4 + H2O
34S is used to discriminate between H2SO4 produced from OH above and ambient H2SO4 – which is also measured
Then detecting via :
[H2SO4] = C
HSO4-
NO3-
[MSA] = C
(CH3)SO3-
NO3-
Where C is a directly measured calibration coefficient
Nitrate Ion Chemical Ionization Mass Spectrometry

## Slide 6
FRAPPE OH

## Slide 7
FRAPPE H2SO4

## Slide 8
What is this “Other Oxidant” Measurement?
OH is measured by first converting it to H234SO4 via:
OH + 34SO2 → H34SO3
H34SO3 + O2 → 34SO3 + HO2
34SO3 + 2H2O → H234SO4 + H2O
and then measuring H234SO4
34S is used to discriminate between H2SO4 produced from OH above and ambient H2SO4 – which is also measured
Additionally other unknown oxidants can also convert SO2 into H2SO4. To account for these processes a second measurement is made by adding a small amount of OH scavenger, propane, to the front injectors.
This second measurement represents other oxidants that can oxidize SO2 to produce H2SO4 but do not react with propane.
The difference in the H234SO4 without and with propane added is attributable to H234SO4 produced OH chemistry.

## Slide 14
Alpha-pinene
sCI
Alpha-Pinene Ozonolysis

## Slide 15
Novelli, A., et al., Identifying Criegee intermediates as potential oxidants in the troposphere, Atm. Chem. Phys. doi:10.5194/acp-2016-919, 2016.
Kim, S., et al., Potential Role of Stabilized Criegee Radicals in Sulfuric Acid Production in a High Biogenic VOC Environment, Environ Sci Technol, 49(6), 3383-3391, doi:Doi10.1021/Es505793t, 2015.
Mauldin, R. L., et al., A new atmospherically relevant oxidant of sulphur dioxide, Nature, 488(7410), 193-197, doi:Doi 10.1038/Nature11278, 2012.
Welz, O., et al, Direct Kinetic Measurements of Criegee Intermediate (CH2OO) Formed by Reaction of CH2I with O2, Science, 335, 204-207, 10.1126/science.1213229, 2012.

## Slide 23
H2SO4 modeling
Assume steady state for H2SO4
Production
kSO2[OH][SO2]
kOx[Other Ox][SO2]
Loss
Diffusion limited aerosol uptake
(4/(au))-1 An a = mass accommodation coefficient
u = molecular speed
A = Fuchs surface area
n = [H2SO4]

## Slide 25
Conclusions
“Other Oxidant(s)” are seen in larger concentrations in areas with urban influences
Usual biogenic suspects for the formation of stabilized Criegee Intermediates don’t seem to correlate with observations.
Possible correlation with CH3OOH – warrants further investigation
Future work
Try to identify class or classes of compounds responsible for Other Oxidant signal
Model H2SO4 and compare with measurement