## Slide 1: Two-dimensional remote sensing of trace gases by the GeoTASO and GCAS airborne instruments during DISCOVER-AQ
Caroline Nowlan, Xiong Liu, Gonzalo Gonzalez Abad, Kelly Chance
Harvard-Smithsonian Center for Astrophysics
James Leitch, Joshua Cole, Tom Delker, Bill Good, Lyle Ruppert, Dan Soo
Ball Aerospace
Scott Janz, Chris Loughner, Melanie Follette-Cook, Matt Kowalewski, Ken Pickering
NASA Goddard Space Flight Center
Alan Fried
INSTAAR, University of Colorado Boulder
Jassim Al-Saadi
NASA Langley Research Center
Jay Herman
NASA Langley Research Center
Lukas Valin and James Szykman
Environmental Protection Agency
FRAPPE/DAQ Science Team Meeting, May 2017

## Slide 2: GeoTASO and GCAS
GeoTASO and GCAS are test-bed instruments for geostationary satellite missions
  Provide test data
  Satellite analog for field campaigns
  Future validation instruments

## Slide 3: GeoTASO and GCAS Instruments
Geostationary Trace gas and Aerosol Sensor Optimization
  Ball Aerospace, now with Scott Janz at NASA GSFC
GEO-CAPE Airborne Simulator
  NASA GSFC follow-on from ACAM (D-AQ Maryland/California) (also led by Scott Janz)
 | GeoTASO | GCAS | TEMPO
Wavelength range | 290 – 400 nm 415 – 695 nm | 300 – 490 nm 480 – 900 nm | 290 – 490 nm 540 – 740 nm
Spectral resolution | 0.43 nm 0.88 nm | 0.58 nm 2.8 nm | 0.57 nm 0.57 nm
Spatial resolution (NO2) | 250 m x 250 m | 250 x 500 m | 2.1 km x 4.4 km
Reference spectrum | Zenith or clean nadir | Clean nadir | Solar diffuser

## Slide 4: Trace Gas Analysis
Two step procedure:
Fit slant columns from spectra
Apply air mass factor to get vertical column
  VLIDORT for radiative transfer calculations
  CMAQ or WRF-Chem for vertical profile shapes

## Slide 5: Algorithm Summary
NASA GSFC (PI: Scott Janz)
  Use WinDOAS (BIRA) spectral fitting package for slant columns
  Slant column data on DISCOVER-AQ archive for:
    ACAM (Maryland 2011, California 2013)
    GCAS (Texas 2013, Colorado 2014)
  Current versions will be updated soon for Texas and Colorado to fix geo-registration
  Plans for GCAS air mass factor calculations (Lok Lamsal, GSFC)
Smithsonian Astrophysical Observatory (Caroline Nowlan and Xiong Liu)
  Use OMI/TEMPO heritage algorithms
  Sub-contracted by Ball Aerospace to provide trace gas retrievals from GeoTASO
  Responsible for ACAM/GCAS research grade product
  SAO provides slant columns, vertical columns, scattering weights at ~250x500 m2

## Slide 6: DISCOVER-AQ Texas GeoTASO NO2
[Nowlan et al., AMT, 2016]
13 September 2013 (Houston AM Flight)

## Slide 7: DISCOVER-AQ Texas GeoTASO NO2
[Nowlan et al., AMT, 2016]

## Slide 8: DISCOVER-AQ Texas GCAS and GeoTASO NO2
13 September 2013 (Houston AM Flight)
[Nowlan et al., AMT, 2016]

## Slide 9: DISCOVER-AQ Texas GCAS Formaldehyde
25 September 2013
2:00 – 3:30 PM LT
GCAS Vertical Columns Averaged over P-3B Spiral Area (all days)

## Slide 10: DISCOVER-AQ Colorado GeoTASO NO2
8:00 – 11:30 AM Local time
2:00 – 4:00 pm local time
Slant
Column
2 August 2014 Raster Scans

## Slide 11: DISCOVER-AQ Colorado GeoTASO NO2
[Luke Valin, EPA]
PANDORA Vertical Columns vs. GeoTASO Slant Columns

## Slide 12: DISCOVER-AQ Colorado GCAS NO2
Slant
Column
2 August 2014
8:00-10:00 LT
2 August 2014
13:10-15:00 LT
2 August 2014
15:00-16:40 LT
2 August 2014
10:00-11:15 LT

## Slide 13: DISCOVER-AQ Colorado GCAS NO2
Slant
Column
2 August 2014
10:00-11:15 LT

## Slide 14: DISCOVER-AQ Colorado GeoTASO SO2
Photo by J.B. Forbes
GeoTASO measured coincident slant columns of NO2 and SO2 downwind from Labadie Power Station, Missouri’s largest coal-burning power plant, on transit from Colorado to Virginia (08/13/2014)

## Slide 15: Data Status and Plans
DISCOVER-AQ Texas
  GeoTASO
    NO2 vertical columns on DISCOVER-AQ archive [Nowlan, et al., AMT, 2016]
    UV absorption suffered from straylight issues
  GCAS
    NO2 and HCHO almost finalized and will be on archive soon
DISCOVER-AQ Colorado
  GeoTASO
    NO2 and SO2 slant columns available upon request
  GCAS
    NO2 and HCHO slant columns available upon request
    Vertical column calculations under way and data should be on archive soon
Future Work
  GeoTASO absolute spectral calibration needs improvement for O3 profile retrievals
  What model or idealized trace gas profiles to use for data in archive?
  Quantifying the effects of aerosols

## Slide 16: DISCOVER-AQ Texas GeoTASO NO2
[Nowlan et al., AMT, 2016]
Inferred surface NO2 using CMAQ